## Slide 1: Vicon RotaFlow RO Disc Spreaders
Arable Systems Division - Crop Care Equipment 2022

## Slide 2: Vicon RO Spreaders
Disc Spreaders
Product information 2021

## Slide 3
Spreading is all about precision and getting the best yield from your crop. Optimal spreading of fertiliser means using exact amounts of nutrition and avoiding overlap.
New opportunities helping you to optimise your income and growth are central focus points. Weather and field conditions are changing continuously, so skills, experience and smart farming systems are decisive factors.
Vicon spreading solutions help you to work in an easier and more profitable way.
These innovative solutions support a better harvest and increased crop yield, because every crop deserves the best care.
Product Story

## Slide 4: Spreader Competence Centre
“Accurate spreading starts here”

## Slide 5
Spreader Competence Centre
Ultra-modern test facility
Highly advanced 3D test system and software set up
Gives quicker availability of spreading charts to set up your spreader in the most accurate way
Movie

## Slide 6: Vicon RO Disc Spreaders
Importance of physical properties

## Slide 7
Distribution (granule size)
Density (kg/l)
Shape and surface
Grain strength
Physical Properties of Fertiliser

## Slide 8
Influence on Distribution
Distribution
  < 2mm (very small = ‘dust’)
  > 4,75mm (very heavy = ‘grid’)
  Ideal = 80% in the middle compartment:
  2 – 4,75mm
  For bigger working widths the most
  granules should be in the compartment
  3,3 – 4,75mm
Always in combination with:
  Density
  Grain strength
  Temperature and humidity (weak granules)

## Slide 9
Influence on Density
Ideal situation is:
  +/- 1 kg/l
  Light: more sensitive for wind influence
  Limitation of maximal spreading width
  Heavy: risk of crop damage

## Slide 10
Influence on Shape and Surface
Resistance:
  ‘Slide’ along each other and through the dosing system
  ‘Roll’ on the vane
  ‘Fly’ in the sky
  Round and smooth: easy flow
Fertiliser properties and limitations:
  Sharp-edged shape means longer travel time on the vanes for wide settings
  To get a correct spreading pattern, also behind the spreader, a ‘small’ setting is needed (e.g. Kali), but for this reason a limitation in maximum working width is needed.

## Slide 11
Influence on Grain Strength
Soft granule is more sensitive for damages
Coating
Working width: gives energy to the granule
Every change of direction: additional impact and resistance
Additional resistance: also additional wearing
Rough surface: additional resistance

## Slide 12
Example of Influence on Distribution
Three times ‘the same’ fertiliser
  KAS 0-15-80-5 with correct settings
  KAS 10-30-60-0, but kept the same setting as for KAS 0-15-80-5
  KAS 15-55-30-0, but kept the same setting as for KAS 0-15-80-5

## Slide 13
CV= 8,5%
CV= 8,4%
CV= 5,4%
WW= 24m
WW= 33m
WW= 39m
KAS 0-15-80-5 with correct settings

## Slide 14
CV= 18,1%
CV= 15,9%
CV= 6,3%
WW= 24m
WW= 33m
WW= 39m
10-30-60-0
KAS 10-30-60-0 but kept same settings as KAS 0-15-80-5

## Slide 15
CV= 27,4%
CV= 20,4%
CV= 7,4%
WW= 24m
WW= 33m
WW= 39m
KAS 15-55-30-0 but kept same settings as KAS 0-15-80-5

## Slide 16
Conclusions from Those Spreading Patterns
Small distribution comes with the same setting less far (wide).
Due to this there is no fertiliser between the tramlines and there is not enough overlap.
How larger the working width, the bigger this effect is.
This does not always mean that it is not possible to spread smaller fertiliser on a specific working width; but that you need adjusted settings on a bigger working width to keep a good spreading pattern.
  -> on smaller working widths the deviation is smaller or ‘invisible’
  -> so on larger working widths the importance of selecting the correct distribution is getting more and more important.
Also when using GPS section control the spreading pattern and settings must be taken into account!

## Slide 17
The RotaFlow Star Checklist for Accurate Spreading
1 Select fertiliser type (shape)
2 Determine granule size and distribution
3 Determine litre weight (kg/l)

## Slide 18
Take your spreading charts book
or
Open http://www.viconspreadingcharts.com
or
Open your spreading charts app on your iPhone or Android phone (free download from the App or Google Play store)
Book
Web
App
1
Choose Your Machine

## Slide 19
Enter the Field Settings
Book
Web
App
2

## Slide 20
Select Fertiliser Type
3

## Slide 21
Select Fertiliser Type
3

## Slide 22
Fill your granule size box with fertiliser
Flip it and shake it well
Determine the granule size and distribution
Determine Granule Size and Distribution
4

## Slide 23
How to Use the Shaker Box?
Movie

## Slide 24
What is the weight of exactly 1 liter?
Determine Litre Weight (Density)
5

## Slide 25
Determine Litre Weight (Density)
5
What is the weight of exactly 1 litre?

## Slide 26
How to Determine the Density?
Movie

## Slide 27
Granule distribution
6
Fill in the Data in the App/web or Find Your Spreading Table in the Book

## Slide 28
Fertiliser type
6
Fill in the Data in the App/web or Find Your Spreading Table in the Book

## Slide 29
Litre weight
6
Fill in the Data in the App/web or Find Your Spreading Table in the Book

## Slide 30
If your brand is not in, please find another one which is with the closest characteristics to yours.
Vicon is always advising to set-up your spreader based on the physical properties of the fertiliser, not the brand!
7
Find Your Fertiliser

## Slide 31
See Your Advised Settings and Enter Them in Your Spreader
8

## Slide 32
...or Use the UNIQUE AutosetApp on the IsoMatch Tellus PRO / GO+
9
Settings automatically via the AutosetApp
Always the most up to date spreading charts online available via the IsoMatch Tellus or Tellus GO
Update via:
  IsoMatch Wireless
  Download on an USB stick
After the selection the settings are automatically send to the spreader
Use granule size box to determine distribution
Determine litre weight
and fertiliser type

## Slide 33
Most close to measured specific weight and granular size distrubtion
Proposal highlighted in red
After sending: Initial values for opening position and theoretical flow at this position is adjusted and Letter setting is changed (in example from « N » to « M »)
AutosetApp

## Slide 34
Spreading Charts
Direct access to the most recent test results at: www.viconspreadingcharts.com
Download the spreading chart application from the Google Play Store or App Store
AutosetApp on IsoMatch Tellus GO+ or IsoMatch Tellus PRO

## Slide 35: The RotaFlow Principle
RotaFlow RO Spreader Range

## Slide 36
The RotaFlow Principle
1
No impact,
No fragmentation
No dust
2
Accurate
spreading pattern
3
Minimal wind influence,
maximum tolerance
4
Consistent spreading
pattern
5
Guaranteed accuracy
on slopes
Central release point, smooth
acceleration and centrifugal force
accelerates fertiliser up to
disc speed before it reaches
the vane.
Large 8 vane discs allow 9 to 45m spread widths. Double overlap spreading pattern gives unrivalled accuray.
Flat discs.
Horizonal spreading pattern
Double overlap spreading pattern.
The fertiliser always contacts the vanes at the same point, also on slopes, and travels the complete length of the vanes.

## Slide 37
The RotaFlow Principle
1
No impact,
No fragmentation
No dust
No falling fertiliser on the vanes but a
smooth acceleration of the granules up
to disc speed by the centrifugal force.
This brings the fertiliser to the central
release point before it reaches the vanes

## Slide 38
Wear of the vanes |  |  |  | 
 | Kg/Ha | Discs | Vanes | Kg/vane/ha
Competition | 400 | 2 | 2 | 100
Vicon | 400 | 2 | 8 | 25
The RotaFlow Principle
2
Accurate
spreading pattern
Large 8 vane discs allow 9 to 54m spread widths. Double overlap spreading pattern gives unrivalled accuracy.

## Slide 39
1
2
3
4
5
7
6
8
The most optimal lateral distribution in the market splitted into 16 sectors (2x8).
Very important by higher forward speed.
Quality of Lateral Distribution
In working width and driving direction
Optimal distribution with 8 vanes per disc
at higher speeds

## Slide 40
The RotaFlow Principle
3
Minimal wind influence,
maximum tolerance
Flat discs.
Horizonal spreading pattern.

## Slide 41
The RotaFlow Principle
Above 24 metre
36 m
24 m
Till 24 metre
4
Double overlap
Trapezium overlap
Trapezium spread pattern with spreader under an angle

## Slide 42
The RotaFlow Principle
5
Guaranteed accuracy on slopes
The fertiliser always contacts the vanes
at the same point, also on slopes, and
travels the complete length of the vanes.
Vicon RotaFlow
Other brands

## Slide 43: FlowPilot
Easy Setting and Adjustment

## Slide 44
Application rate setting:
EasySet System
EasySet system
RO-M / RO-XL
Fine application rate setting
Discharge point
RO-M / RO-M-E / RO-M EW / RO-XL / RO-XL-E / RO-EDW / RO-XXL (GEOSPREAD)
RO-M / RO-M-E / RO-M EW / RO-XL/ RO-XL-E / RO-EDW / RO-XXL
RO-M / RO-M-E / RO-M EW / RO-XL / RO-XL-E / RO-EDW / RO-XXL (GEOSPREAD)

## Slide 45
Adjustment RotaFlow Spreaders
RO-M / RO-XL
RO-M-E/ RO-M EW /
RO-XL-E / RO-EDW / RO-XXL
GEOSPREAD®
RO-C
1 electric actuator for application rate
2 electric actuators for application rate and discharge point

## Slide 46
Spreader Settings RO-C
Discharge point
Application rate

## Slide 47
How to Adjust Your RO-C Spreader?
Movie

## Slide 48
Adjustment RO-M
Discharge point
Application rate
Fine application

## Slide 49
Spreader Settings RO-M-E / RO-M EW
Discharge point
Fine application

## Slide 50
How to Adjust Your RO-XL E / RO-M-E / RO-M-EW Spreader?
Movie

## Slide 51
Spreader Settings RO-XL
Discharge point
Application rate
Fine application

## Slide 52
Spreader Settings RO-EDW
Discharge point
Fine application
Application rate
Automatic adjustment of:

## Slide 53
How to Adjust the Settings of a Weighing Spreader via an ISOBUS terminal?
Movie

## Slide 54
How to Adjust the Settings of a Weighing Spreader via an IsoMatch Tellus Terminal?
Movie

## Slide 55
Adjustment RO-M/RO-EDW/RO-XXL GEOSPREAD®
Discharge point
Fine application
Application rate
Automatic adjustment of:

## Slide 56
How to Adjust the GEOSPREAD® Spreader Settings via an ISOBUS Terminal?
Movie

## Slide 57
How to Adjust the GEOSPREAD® Spreader Settings via an IsoMatch Tellus Terminal?
Movie

## Slide 58
Vicon Disc Spreader Range
Comfort Level – Ease of Use

## Slide 59
Vicon Disc Spreader Range
Comfort Level – Ease of Use

## Slide 60: Vicon RO-C Spreaders
Double Disc Spreader

## Slide 61: RO-C 700 – 900 – 1400
 | RO-C 700 | RO-C 900 | RO-C 1400
Hopper capacity (l) | 700 | 900 | 1400
Filling height (cm) | 96 | 108 | 128
Width (cm) | 154 | 154 | 176
Filling width (cm) | 148 | 148 | 170
Empty weight (kg) | 250 | 270 | 290
Spread width (m) | 9-18 (20/21)* | 9-18 (20/21)* | 9-18 (20/21)*
Output (kg/min) | 10-230 | 10-230 | 10-230
*with optional set of vanes
Overview
Movie

## Slide 62
Three options of hopper capacity
700 – 900 – 1,400 litres
Hydraulic control
Four detachable vanes per disc
determine the working width
RotaFlow system

## Slide 63
RotaFlow RO-C
Standard features
Right hand spreading disc can be shut off
Overload clutch
Stainless steel hose connections
Robust steel sieves
Tool to open the sieves
Grading box to test the fertiliser quality
Four hopper windows
All vanes for 9-18 m (4 vanes per disc)
With longer vanes 21m working width is possible

## Slide 64: Vicon RO-M Spreaders
Double Disc Spreader

## Slide 65: RO-M 1100 – 1550 – 2000
 | RO-M 1100 | RO-M 1550 | RO-M 2000
Hopper capacity (l) | 1100 | 1550 | 2000
Filling height (cm) | 100 | 119 | 138
Width (cm) | 220 | 220 | 220
Filling width (cm) | 214 | 214 | 214
Empty weight (kg) | 325 | 350 | 375
Spread width (m) | 10-24 (27/28)* | 10-24 (27/28)* | 10-24 (27/28)*
Output (kg/min) | 10-320 | 10-320 | 10-320
*with optional set of vanes
Overview

## Slide 66
Hydraulic control
Three options of hopper capacity
1,100 – 1,550 – 2,000 litres
Easy to assemble
aluminium hopper
extension
FlowPilot: for accurate setting and adjustment of applicaiton rates
RotaFlow system with 8 vanes per disc
Set the right application rate and increase or decrease the application on the move
Both spreading discs can be shut off
independently to spread half the working width
Electric actuator to control the application rate

## Slide 67
RotaFlow RO-M
Standard features
Fine application kit
Overload clutch
Stainless steel hose connections
2 Delta shaped heavy duty grids
Tool to open the sieves
Grading box to test the fertiliser quality
Four hopper windows
All vanes for 10-24 m
With longer vanes 28m working width is possible

## Slide 68
RO-M Hydraulic Operated
RO-M
Operation with double acting valve on
tractor
Stainless steel hose connections
Application setting in 90 steps
Open/close indicator
RO-M E

## Slide 69: Vicon RO-M ”Easy Weigh” Spreader
Weighing Spreader

## Slide 70: RO-M EW 1100 – 1550 – 2000
 | RO-M EW 1100 | RO-M EW 1550 | RO-M EW 2000
Hopper capacity (l) | 1100 | 1550 | 2000
Filling height (cm) | 100 | 119 | 138
Width (cm) | 220 | 220 | 220
Filling width (cm) | 214 | 214 | 214
Empty weight (kg) | 380 | 400 | 425
Spread width (m) | 10-24 (27/28)* | 10-24 (27/28)* | 10-24 (27/28)*
Output (kg/min) | 10-320 | 10-320 | 10-320
*with optional set of vanes
Overview

## Slide 71
Three options of hopper capacity
1,100 – 1,550 – 2,000 litres
Easy to assemble aluminium hopper extensions
10 tonne load cell + reference sensor
RotaFlow system
with 8 vanes per disc
AEF certified – ISOBUS compatible spreader
TC-SC ISOBUS section control

## Slide 72
RotaFlow RO-M EW Easy Weigh
Standard features
Best weighing results and dosing control: unique in it’s segment!
Integrated weighing system
1x 10 ton load cell with reference sensor
Standard full ISOBUS compatible
Compact design: gravity point stays close to tractor
Tool to open the sieves
All vanes for 10-24 m
With longer vanes 28m working width is possible
  SPREADERcontrol license option:
  Basic Section Control
  Max. 7 sections of 4m

## Slide 73: Vicon RO-XL Spreaders
Double Disc Spreader

## Slide 74: RO-XL 1500 – 2150 – 2800 – 3450
 | RO-XL 1500 | RO-XL 2150 | RO-XL 2800 | RO-XL 3450
Hopper capacity (l) | 1500 | 2150 | 2800 | 3450
Filling height (cm) | 110 | 129 | 148 | 167
Width (cm) | 275 | 275 | 275 | 275
Filling width (cm) | 269 | 269 | 269 | 269
Empty weight (kg) | 495 | 495 | 495 | 495
Spread width (m) | 12-54* | 12-54* | 12-54* | 12-54*
Output (kg/min) | 10-320 | 10-320 | 10-320 | 10-320
*with optional lift vanes
Overview

## Slide 75: RO-XL 1875 – 2550 – 3225 – 3900
 | RO-XL 1875 | RO-XL 2550 | RO-XL 3225 | RO-XL 3900
Hopper capacity (l) | 1875 | 2550 | 3225 | 3900
Filling height (cm) | 120 | 139 | 158 | 177
Width (cm) | 290 | 290 | 290 | 290
Filling width (cm) | 284 | 284 | 284 | 284
Empty weight (kg) | 530 | 565 | 595 | 625
Spread width (m) | 12-54* | 12-54* | 12-54* | 12-54*
Output (kg/min) | 10-320 | 10-320 | 10-320 | 10-320
*with optional lift vanes
Overview

## Slide 76
Hydraulic control
Two options of basic hopper capacity 1,500 or 1,875 litres, can be extended with easy to assemble aluminium
hopper extentions
Long life time
LED lighting set
FlowPilot: for accurate setting and adjustment of application rates
Slow rotating agitator
RotaFlow system with
8 vanes per disc

## Slide 77
RotaFlow RO-XL
Standard features
Stainless steel front plates
Fine application kit
Overload clutch
Stainless steel hose connections
2 High capacity & robust sieves
Tool to open the sieves
Inclinometer
Grading box to test the fertiliser quality
Open/close indicator
Top and bottom hopper windows
Low speed agitator (15%)
LED lighting set
Lift vanes
Standard vanes

## Slide 78
RO-XL Hydraulic Operated
Operation with double acting valve on tractor
Stainless steel hose connections
Application setting in 90 steps
Open/close indicator
RO-XL
RO-XL E

## Slide 79: Vicon RO-EDW Spreader
Weighing Spreader

## Slide 80
Weighing Frame RO-M/RO-EDW/RO-XXL (GEOSPREAD)
5 ton load cell – RO-EDW
Reference sensor
2,5 ton load cell – RO=M
5 ton load cell – RO-EDW
2,5 ton load cell – RO=M
5 ton load cell – RO-EDW
2,5 ton load cell – RO=M
5 ton load cell – RO-EDW
2,5 ton load cell – RO=M

## Slide 81
Continuous Weighing with Vicon
Signal from the load cells
Signal from the reference sensor
Automatic correction of shocks
Vicon’s unique reference sensor technology: all negative influences (shocks, bouncing, speeding up / slowing down, inclination) are corrected and eliminated, ensuring utmost spreading accuracy in all conditions.
Continuous dynamic ‘online – calibration’ with high frequency communication signal.

## Slide 82
Auto calibrating and continuous weighing system
Automatic correction on slopes
Automatic correction of shocks, even on rough terrain
Automatic speed related dosing system
No calibration test needed
Accurate weighing during spreading NON-STOP
Technology of 21st century
Weighing system is not influenced in hilly conditions, speed change
Possible continues auto calibration
Increasing accuracy in every conditions
Eliminating influence of changing fertiliser properties
Exact documentation how much you spread
Online control
Continuous Weighing with Vicon
Load cells in combination with the unique reference sensor

## Slide 83: RO-EDW 1500 – 2150 – 2800 – 3450
 | RO-EDW 1500 | RO-EDW 2150 | RO-EDW 2800 | RO-EDW 3450
Hopper capacity (l) | 1500 | 2150 | 2800 | 3450
Filling height (cm) | 110 | 129 | 148 | 167
Width (cm) | 275 | 275 | 275 | 275
Filling width (cm) | 269 | 269 | 269 | 269
Empty weight (kg) | 665 | 695 | 725 | 755
Spread width (m) | 12-54* | 12-54* | 12-54* | 12-54*
Output (kg/min) | 10-320 | 10-320 | 10-320 | 10-320
*depending on vanes and type of fertiliser
Overview

## Slide 84: RO-EDW 1875 – 2550 – 3225 – 3900
 | RO-EDW 1875 | RO-EDW 2550 | RO-EDW 3225 | RO-EDW 3900
Hopper capacity (l) | 1875 | 2550 | 3225 | 3900
Filling height (cm) | 120 | 139 | 158 | 177
Width (cm) | 290 | 290 | 290 | 290
Filling width (cm) | 284 | 284 | 284 | 284
Empty weight (kg) | 705 | 735 | 765 | 795
Spread width (m) | 12-54* | 12-54* | 12-54* | 12-54*
Output (kg/min) | 10-320 | 10-320 | 10-320 | 10-320
*depending on vanes and type of fertiliser
Overview

## Slide 85
Long life time
LED lighting set
RotaFlow system with 8 vanes per disc
Two options of basic hopper capacity 1,500 or 1,875 litres, can be extended with easy to assemble aluminium hopper extensions
AEF certified – ISOBUS
compatible spreader
TC-SC ISOBUS section control

## Slide 86
RotaFlow RO-EDW
Standard features
  Constant weighing of the output
  ISOBUS compatible
  Stainless steel front plates
  Fine application kit
  Overload clutch
  Tool to open the sieve
  Inclinometer
  Stainless steel hose connections
  2 High capacity & robust sieves
  Grading box to test the fertiliser quality
  Top and bottom hopper windows
  Low speed agitator (15%)
  LED lighting set
  SPREADERcontrol License option:
  Basic Section Control
  Max. 14 sections of 4m
Lift vanes
Standard vanes

## Slide 87: Vicon RO-M GEOSPREAD®
Weighing Spreaders

## Slide 88: RO-M GEOSPREAD® 1100 – 1550 – 2000 – 2450
 | RO-M 1100 GEOSPREAD | RO-M 1550 GEOSPREAD | RO-M 2000 GEOSPREAD | RO-M 2450 GEOSPREAD
Hopper capacity (l) | 1100 | 1550 | 2000 | 2450
Filling height (cm) | 108 | 127 | 146 | 165
Width (cm) | 220 | 220 | 220 | 220
Filling width (cm) | 214 | 214 | 214 | 214
Empty weight (kg) | 483 | 506 | 529 | 552
Spread width (m) | 10-24 (27/33)* | 10-24 (27/33)* | 10-24 (27/33)* | 10-24 (27/33)*
Output (kg/min) | 10-320 | 10-320 | 10-320 | 10-320
*depending on type of fertiliser and vanes
Overview

## Slide 89: RO-M GEOSPREAD® 1300 – 1800 – 2300 – 2800
 | RO-M 1300 GEOSPREAD | RO-M 1800 GEOSPREAD | RO-M 2300 GEOSPREAD | RO-M 2800 GEOSPREAD
Hopper capacity (l) | 1300 | 1800 | 2300 | 2800
Filling height (cm) | 113 | 132 | 151 | 170
Width (cm) | 245 | 245 | 245 | 245
Filling width (cm) | 239 | 239 | 239 | 239
Empty weight (kg) | 495 | 520 | 545 | 570
Spread width (m) | 10-24 (27/33)* | 10-24 (27/33)* | 10-24 (27/33)* | 10-24 (27/33)*
Output (kg/min) | 10-320 | 10-320 | 10-320 | 10-320
Overview
*depending on type of fertiliser and vanes

## Slide 90
Two options of basic hopper capacity 1,100 or 1,300 litres, can be extended with easy to assemble aluminium hopper extensions
AEF certified –
ISOBUS compatible spreader
Slow rotating agitator
GEOSPREAD®: Two actuators to control the discharge point and application rate
RotaFlow system
with 8 vanes per disc
4x 2,5 tonne load cells + reference sensor

## Slide 91: Vicon RO-EDW GEOSPREAD®
Weighing spreader

## Slide 92
Vicon RO-EDW GEOSPREAD® 1500-2150-2800-3450
 | RO-EDW 1500 | RO-EDW 1500 - 2150 | RO-EDW 1500 - 2800 | RO-EDW 1500 – 3450
Hopper capacity (l) | 1500 | 2150 | 2800 | 3450
Filling height (cm) | 123 | 142 | 161 | 180
Width (cm) | 290 | 290 | 290 | 290
Filling width (cm) | 284 | 284 | 284 | 284
Empty weight (kg) | 655 | 685 | 715 | 745
Spread width (m) | 12-54* | 12-54* | 12-54* | 12-54*
Output (kg/min) | 10-320 | 10-320 | 10-320 | 10-320
*depending on type of fertiliser and vanes
Overview
Movie

## Slide 93
Vicon RO-EDW GEOSPREAD® 1875-2550-3225-3900
 | RO-EDW 1875 | RO-EDW 1875 - 2550 | RO-EDW 1875 - 3225 | RO-EDW 1875 - 3900
Hopper capacity (l) | 1875 | 2550 | 3225 | 3900
Filling height (cm) | 123 | 142 | 161 | 180
Width (cm) | 290 | 290 | 290 | 290
Filling width (cm) | 284 | 284 | 284 | 284
Empty weight (kg) | 695 | 725 | 755 | 785
Spread width (m) | 12-54* | 12-54* | 12-54* | 12-54*
Output (kg/min) | 10-320 | 10-320 | 10-320 | 10-320
*depending on type of fertiliser and vanes
Overview

## Slide 94
Two options of basic hopper capacity 1,500 or 1,875 litres, can be extended with easy to assemble aluminium hopper extensions
AEF certified – ISOBUS compatible spreader
RotaFlow system with 8 vanes per disc
GEOSPREAD®: Two actuators to control the discharge point and application rate
4x 5 tonne load cell
+ reference sensor
TC-SC ISOBUS section control

## Slide 95: Vicon RO-XXL GEOSPREAD®
High speed weighing spreader

## Slide 96
Vicon RO-XXL GEOSPREAD® 1875-2550-3225-3900
 | RO-XXL 1875 | RO-XXL 2550 | RO-XXL 3225 | RO-XXL 3900
Hopper capacity (l) | 1875 | 2550 | 3225 | 3900
Filling height (cm) | 123 | 142 | 161 | 180
Width (cm) | 290 | 290 | 290 | 290
Filling width (cm) | 284 | 284 | 284 | 284
Empty weight (kg) | 705 | 735 | 765 | 795
Spread width (m) | 24-40* | 24-40* | 24-40* | 24-40*
Output (kg/min) | 10-540 | 10-540 | 10-540 | 10-540
*depending on type of fertiliser and vanes
Overview
Movie

## Slide 97
Four options of hopper capacity
1,875 – 2,550 – 3,225 – 3,900 litres
AEF certified – ISOBUS compatible spreader
High speed RotaFlow system with 8 vanes per disc
GEOSPREAD®: Two actuators to control the discharge point and application rate
Working width: 24-45 metres
4x 5 tonne load cell
+ reference sensor

## Slide 98
High speed spreading under all circumstances.
Newly designed RotaFlow system with 8 high capacity vanes on each disc for a perfect overlap, no matter how fast you are driving.
RO-XXL GEOSPREAD®

## Slide 99: GEOSPREAD® System
RO-M GEOSPREAD®, RO-EDW GEOSPREAD®,
RO-XXL GEOSPREAD®

## Slide 100
Standard features
Additional 2 actuators on each spreading disc
GPS section control in minimum 1m wide sections
GEOSPREAD®
Movie

## Slide 101
Two actuators on each dosing unit
  one controls the discharge point
  second controls the application rate
Adjust letter setting individually from the tractor cab
Automatic start/stop with GPS on head lands possible
TS-SC ISOBUS section control
GEOSPREAD® System

## Slide 102
Working width will be automatically adjusted to suit the overlap and coverage using a GPS positioning system.
GEOSPREAD® is using the section control function of the IsoMatch GEOCONTROL® software which is in the IsoMatch Tellus GO+ or IsoMatch Tellus PRO terminal.
Spreader working width is divided into a maximum of:
CL GEOSPREAD® - 33* sections of 1 metre
TL GEOSPREAD and TLX GEOSPREAD® 54* sections of 1 metre
Not only the spreading width is adjusted, the application rate (kg/min) is also adjusted automatically to match the revised spreading width.
IsoMatch GEOCONTROL® in Combination with GEOSPREAD®
* - max number of sections alsways depends on the terminal task controller

## Slide 103
Example: Full spreading width 24m with 24 sections*
GPS Controlled Intelligent Machine Solutions
*Using IsoMatch GEOCONTROL® in combination with RO-EDW and RO-XXL GEOSPREAD®

## Slide 104
Decreasing the spreading width on the left hand side by 3 m*
GPS Controlled Intelligent Machine Solutions
*Using IsoMatch GEOCONTROL® in combination with RO-EDW and RO-XXL GEOSPREAD®

## Slide 105
Decreasing the spreading width on the left hand side by 5 m*
GPS Controlled Intelligent Machine Solutions
*Using IsoMatch GEOCONTROL® in combination with RO-EDW and RO-XXL GEOSPREAD ®

## Slide 106
Decreasing the spreading width on both sides by 4 m*
GPS Controlled Intelligent Machine Solutions
*Using IsoMatch GEOCONTROL® in combination with RO-EDW and RO-XXL GEOSPREAD®

## Slide 107
Switching off the sections outwards*
GPS Controlled Intelligent Machine Solutions
*Using IsoMatch GEOCONTROL® in combination with RO-EDW and RO-XXL GEOSPREAD®

## Slide 108
Switching the sections over the middle from one side*
GPS Controlled Intelligent Machine Solutions
*Using IsoMatch GEOCONTROL® in combination with RO-EDW and RO-XXL GEOSPREAD®

## Slide 109
Section control based on ISOBUS protocol
The RO-M GEOSPREAD® has maximum 33 sections, minimum 1m wide
The RO-EDW GEOSPREAD® has maximum 54 sections, minimum 1m wide
Percentage of overlap adjustable from 0-100%
24 sections with no overlap 24 sections with full overlap
GEOSPREAD® Sections

## Slide 110
Quick and accurate spreading, with the discharge point being controlled by actuators.
The small 1 metre sections can be switched inside-out and outside-in to keep overlap to the minimum.
Stable disc RPM in combination with discharge point adjustment maintains the spreading pattern
Easy operation: no need to leave the tractorcab to adjust the working width
100% ISOBUS compatible for easy operation
Advantages GEOSPREAD ®

## Slide 111
Measured in the Spreader Competence Centre.
The spreader will automatically start and stop when the GEOPOINT® is at the edge of the field.
Centre of the 3D spreading pattern is used for optimum performance when opening and closing the dosing system on headlands.
The GEOPOINT® can be found in the spreading charts and will be set automatically when using the AutosetApp.
GEOPOINT®

## Slide 112: Automatic Section Control
RO-M EW and RO-EDW

## Slide 113
Examples of 24 metre working width
Types of Section Control
Conventional spreading Basic Section Control GEOSPREAD®

## Slide 114
Working Principle
Basic Section Control GEOSPREAD®

## Slide 115
Performance of GEOSPREAD® and Basic Section Control
Basic Section Control GEOSPREAD®

## Slide 116
Basic Section Control – Sections/Working Width Example
RO-M EW
18 m 4m / 5m / 5m / 4m
20 m 4m / 6m / 6m / 4m
21 m 4m / 6.5m / 6.5m / 4m
RO-M EW
16 m 4m / 4m / 4m / 4m

## Slide 117
Basic Section Control – Sections/Working Width Example
RO-M EW
24 m 4m / 4m / 4m / 4m / 4m / 4m
RO-M EW
28 m 4m / 4m / 6m / 6m / 4m / 4m

## Slide 118
Basic Section Control – Sections/Working Width Example
RO-M EW
28m in combination with central border spreading plate, 8 sections are possible 4m / 4m / 4m / 2m / 2m / 4m / 4m / 4m

## Slide 119
Basic Section Control – Sections/Working Width Example
RO-EDW 48 m - 12 x 4 m
4m / 4m / 4m / 4m / 4m / 4m / 4m
RO-EDW 54 m 12 + 2 in the middle in case of central border spreading plate is used

## Slide 120: Control Systems
RotaFlow RO Spreader Range

## Slide 121
Application rate setting with control box
12 v power needed
RO-M E / RO-XL E Comfort Control II
Application rate setting
Central and L&R separate over/under dosing
Separate R/L and open/close
Calibration program
RO-M E / RO-XL E
RO-M / RO-XL

## Slide 122
All Our Weighing Spreaders are Standard ISOBUS Compatible
+

## Slide 123
International standard: plug and play functionality between terminal and spreader, when AEF certified!
Free Compatibility check via AEF Database
Supported Features:
*/** may need a license activation code on both Terminal and/or implement
ISOBUS Compatible Spreaders
UT | Universal Terminal | 
TECU | Tractor ECU | 
AUX-N | Auxiliary Control “NEW” | 
TC-BAS | Task Controller basic functionality | (ISO-XML data exchange, as applied totals, hr, kg, etc.)
TC-GEO* | Task Controller geo-based | (location data, Variable Rate application maps)
TC-SC** | Task Controller Section Control** | 

## Slide 124
Terminal |  | Spreader | 
 | License | None | SPREADERCONTROL
iM Tellus (PRO) | None | UT, TC-BAS | UT, TC-BAS, TC-GEO TC-SC
 | GEOCONTROL® | UT, TC-BAS, TC-GEO | UT, TC-BAS, TC-GEO TC-SC
iM Tellus GO | None | UT, TC-BAS, | UT, TC-BAS, TC-GEO TC-SC
 | GEO-VR | UT, TC-BAS, TC-GEO | UT, TC-BAS, TC-GEO
 | GEO-SC | UT, TC-BAS, TC-GEO | UT, TC-BAS, TC-GEO TC-SC
 | GEO-VR + GEO-SC | UT, TC-BAS, TC-GEO | UT, TC-BAS, TC-GEO TC-SC
Terminal & Spreader Functionality
Based on Licenses
Everything about ISOBUS and AEF: www.aef-online.org / www.aef-isobus-database.org

## Slide 125
1
2
ISOBUS Communication System
ISOBUS Communication System
ISOBUS tractor
If the tractor already has an ISOBUS 11783 compatible terminal, there is no need for any additional terminal.
IsoMatch Tellus PRO
For tractors with or without an ISOBUS 11783 terminal a IsoMatch Tellus PRO terminal in combination with the necessary additional cables gives the possibility to operate all ISOBUS 11783 compliant implements from any manufacturer.
IsoMatch Tellus GO+
The IsoMatch Tellus GO+ is a Universal ISOBUS Terminal. This multifunctional one-screen terminal has been developed for fast and simple control of any ISOBUS implement, giving the farmer a ‘custom made’ experience as it suits all needs for simple and efficient handling of farming machinery and tasks.

## Slide 126
IsoMatch Tellus GO+
State of art: dual core processor
  Faster boot time (compared to IsoMatch Tellus GO)
  Faster response time (compared to IsoMatch Tellus GO)
  Capable of handling more and more demanding applications
Glossy display
Supporting IsoMatch Wireless
  Enabling Wi-Fi functionality
Ready to evolve with new functions, features and APP’s
  IsoMatch FarmCentre

## Slide 127
IsoMatch Tellus PRO Universal Terminal
Two ISOBUS interface screens
Large 12.1” colour touch screen
Intuitive operation
Basic DOC registration program to save operational information directly to USB
Four USB slots for easy data exchange, wireless USB stick or USB to serial cable
Built in PDF reader
RS232 connection for GPS receivers or sensors
Internet connection via a wireless USB stick or router
Integrated web browser

## Slide 128
Multi Functional Terminal
Camera
IsoMatch GEOCONTROL®
Touch screen
2 ISOBUS machines
PDF reader
Calculator

## Slide 129: IsoMatch GEOCONTROL®
Additional Software Application within the IsoMatch Tellus

## Slide 130
IsoMatch GEOCONTROL®
Section control Automatic switching on and off implement sections on headlands, boundaries and already covered areas to minimise overlap

## Slide 131
In the IsoMatch Tellus GO+ this license key is divided in two parts, separate available from the IsoMatch Shop. Customers can buy just the functionality they need.
  IsoMatch GEO-SC  automatic section control
  Sector and headlands control distributed in up to 24 sections depending on the implement to which it is connected.
  IsoMatch GEO-VR  automatic variable rate control
  Variable rate control based on data provided by prescription maps or external sensors. Single channel in the entire working width.
  Working range is 2 km from starting point
IsoMatch GEOCONTROL®
Licenses Tellus GO+

## Slide 132
In the IsoMatch Tellus Pro there is 1 license key which is called IsoMatch GEOCONTROL®
It combines the 2 functionalities below
  Automatic section control
  Section and headlands control distributed in up to 88 sections depending on the implement to which it is connected.
  Automatic variable rate control
  Variable rate control based on data provided by prescription maps or external sensors. Single channel in the entire working width.
  Working range is 10 km from starting point
IsoMatch GEOCONTROL®
Licenses IsoMatch Tellus Pro

## Slide 133: MULTIRATE
Next Step in Variable Rate Application

## Slide 134
IsoMatch GEOCONTROL®
Variable rate control
Automatically adjusts the implement application rate based on input from the field prescription
The IsoMatch Tellus PRO requires field maps in ISO-XML format.
The task map is displayed in the IsoMatch GEOCONTROL® screen
To operate variable rate application with two or more rates a licence must be activated
Spreaders with software version 1.20 and higher support MULTIRATE

## Slide 135
The input rate is determined at the GEOPOINT®. The value in the Variable Rate map provides a value of 170 kg/ha.
But the spreader covers area on the map with 150 kg/ha till 195 kg/ha input rate as well.
The deviation from the VRA map is -25 till +20 kg/ha.
The average deviation on the left disc is -21 kg/ha.
The average deviation and for the right disc +10 kg/ha.
Example single rate
IsoMatch GEOCONTROL®

## Slide 136
The input rates are determined at the middle of the left and right of the spreader “boom”. The Variable Rate map provides different values of (190 vs 170 kg/ha) for the left and right disc.
The deviation from the VRA map is reduced to -5 till +20 kg/ha.
The average deviation for the left disc is reduced to -1,2 kg/ha and for the right disc to +10 kg/ha.
Example MULTIRATE 2 rates
IsoMatch GEOCONTROL®

## Slide 137
The input rates are determined at 8 points at the spreader “boom”. The VRA map provides different values of (192 vs 160 kg/ha) for the left and right disc.
The deviation from the VRA map is reduced to -10 till +10 kg/ha.
The average deviation for the left disc is reduced to +0,8 kg/ha and for the right disc to +0 kg/ha.
Example MULTIRATE 8 rates
IsoMatch GEOCONTROL®

## Slide 138
IsoMatch GEOCONTROL®
Documentation All documentation and data can be exchanged between farm management system and IsoMatch GEOCONTROL® via an USB stick.

## Slide 139
Manual guidance
Advised driving position using guidance lines in the field and on headlands
Extendable using the optional IsoMatch InLine light bar, to place guidance in line of sight
Smart boundary recording: independent from the working width, even without any implement corrected
Boundary shrinking: create new inner boundaries by setting de desired width of the headland
Manual guidance for all operations
IsoMatch GEOCONTROL®

## Slide 140
AutosetApp (included in IsoMatch GEOCONTROL® v1.9)
The most up to date setting for your weighing spreader are always online available
The AutosetApp connects the IsoMatch Tellus PRO and IsoMatch Tellus GO+ terminal directly with the Vicon weighing spreader and will automatically adjust the spreader according to the settings entered into the App.
IsoMatch GEOCONTROL®
Movie

## Slide 141
Always the latest online spreading charts available via IsoMatch Tellus PRO or IsoMatch Tellus GO+
Update by:
  IsoMatch wireless
  Download on USB memory stick
Forward the settings from the spreading chart to the spreader and adjust it automatically
AutosetApp

## Slide 142
Easy and comfort of operation, due to not having to manually switch on or off sections or change the application rate. You can focus 100% on the driving in the field.
More efficient work and avoiding overlap leads to cost savings of 5-10% on e.g. fertiliser.
With IsoMatch GEOCONTROL®, working at night time becomes very easy. IsoMatch GEOCONTROL® reduces the workload considerably.
IsoMatch GEOCONTROL®: Brings Clear Benefits

## Slide 143
Spreading at Night!

## Slide 144
IsoMatch Global 3
IsoMatch Global 3 is a GPS antenna and replaces the well known IsoMatch Global.
It provides DGPS signal to the IsoMatch terminals with an accuracy of 40 cm pass to pass.
It works with satellite constellations L1 GPS, G1 GLONASS, E1 Galileo, and B1 BeiDou.

## Slide 145
DGPS accuracy (40 cm pass to pass).
Simple installation on tractor roof. Magnetic support delivered with the standard package.
One single cable to connect to IsoMatch Terminals. Plug and Play functionality.
LED for signal status
  Blinking Red - Power on
  Blinking Amber - GNSS position available
IsoMatch Global 3
Technical specifications

## Slide 146
IsoMatch Eye
Working in the dark possible
View of 120°

## Slide 147
Distance to A-B line with LED indication and numeric display
Manual guidance in combination with IsoMatch GEOCONTROL®
Displays status of machine sections
IsoMatch InLine

## Slide 148
Internet connection to any available wireless network
No additional costs from the internet service provider
Browsing on the spot
Only available in the EU/USA
IsoMatch WireLess

## Slide 149
In combination with IsoMatch Tellus PRO or IsoMatch Tellus GO
Up till 44 functions divided over 4 modes can be programmed to cover the spraying needs
Fully ISOBUS compatible
IsoMatch Grip

## Slide 150
IsoMatch FarmCentre
Data Flow
Dongle
WiFi or Mobile

## Slide 151
Benefits of IsoMatch FarmCentre
Always Connected
  With your device, stay fully up to date on what is happening on your farm
Wireless Transfer of Task Data
  Exchange of Taskdata with Farm Management System
  Planned tasks, Finished tasks
  Variable rate application maps
  Field boundaries
Documentation
  Increased efficiency as less time is spent on administrating tasks
  Service support
  Report alarms & notifications

## Slide 152: Others
Standard Equipment and Accessories

## Slide 153
Vicon Disc Spreader NEWS for 2022

## Slide 154
Improved clean ability of the RO-EDW/RO-XXL GEOSPREAD
  Remove some plastic parts and exchange them with stainless steel
  Implement a solution to open the rear bumper for easier cleaning
Improved overall quality & reliability of the spreader
  Central gearbox: bearings / gears + paint quality (changed colour from light grey to dark grey)
  Better side gearboxes: bearings / gears + paint quality (changed colour from light grey to dark grey)
  Change from 2 tons to 2.5 tons weight load cells on RO-M 1100/1300 GEOSPREAD spreader range
Prepare all the GEOSPREAD spreaders models for the future
  EDW3 pcb – not available because of needed electronic parts are not available
Spreader Update 2022

## Slide 155
Clean ability:
Bumper unfolding for easier access with high pressure cleaner
Mudguards shape & way of fitting
Dashboard simplification on all GEOSPREAD models stainless steel + less corners
Spreader Update 2022

## Slide 156
Quality & reliability improvements:
Central gearbox with new bearings setup and new technology od casting and painting procedure to improve the paint quality
Side gearboxes with changed paint to dark grey
Stronger 2,5 tons load cells instead of 2,0 tons and stainless steel bolts on the RO-M GEOSPREAD 1100/1300
Actuator supplier change from LINAK to TiMOTION
Spreader Update 2022

## Slide 157
Prepared for the future:
EDW3 on all GEOSPREAD spreader models
  Faster processor speed and need on the high spec machines
Diagnostic plug added
  Easier diagnostic & software flashing – direct connection of PCB EDW3 to TopService
Patented electric hopper cover design
Spreader Update 2022
GEOSPREAD EDW3

## Slide 158: Spreader Update 2022
Machine Features: NEW front lighting
Including road signs for transport of a front spreader on public roads
LED lights (no working lights)

## Slide 159: Spreader update 2022 - overview
Available from Q3-4 of 2022

## Slide 160
Standard Range of Vanes (Straight)
RO-C
RO-M / RO-M EW

## Slide 161
Standard Range of Vanes (Straight)
RO-M GEOSPREAD
RO-XL / RO-EDW / RO-EDW GEOSPREAD

## Slide 162
Standard Range of Vanes (Straight)
RO-XXL GEOSPREAD
85 3 3/8"

## Slide 163
RO-XL / RO-EDW / RO-EDW GEOSPREAD
HD carbon hardened - KTL painted black
Optional Range of Vanes (HD Straight)

## Slide 164
  For spreading width up to 54m
  Spreading Urea up to 36m
  Only dedicated spreading tables
  DUPLEX Stainless steel
  Only for HL/TL/TLX/ GEOSPREAD®
  Possible in combination with ExactLine border spreading system
Lift Vanes

## Slide 165
  More wear resistant (Tunghsten carbide) lift vanes for RO-XL/RO-EDW/RO-XXL (GEOSPREAD)
  For hard granules, high flow (rate & working width) i.c.w. a lot of hectares
Heavy Duty Vanes (Coated)
Heavy Duty Vanes (Hardened)
  More wear resistant (carbonised - hardened) straight vanes for RO-XL/RO-EDW (GEOSPREAD)
  For hard granules and high flow (rate & working width) i.c.w. a lot of hectares

## Slide 166
RO-XL / RO-EDW / RO-EDW GEOSPREAD
Duplex or HD (carbide coated)
Optional Range of Vanes (Lift Vanes)
330 13 "

## Slide 167
RO-XXL GEOSPREAD
Duplex or HD (carbide coated)
Optional Range of Vanes (Lift Vanes)
330 13 "
230 9 1/16"

## Slide 168
Range of Vanes - Total Overview
 |  | RO-C | RO-M | RO-M EW | RO-M GEOSPREAD | RO-XL | RO-EDW/RO-EDW GEOSPREAD/RO-EDW iDC | RO-XXL GEOSPREAD
Stainless Steel - straight | STANDARD / OPTION | STANDARD | STANDARD | STANDARD | STANDARD | STANDARD | STANDARD | STANDARD
 | Length (mm) | 2 x 135/185/235 | 2 x 135/185/235/285 | 2 x 135/185/235/285 | 2 x 135/185/235/285 | 2 x 285/285/285 | 2 x 285/285/285 | 2 x 85/285/285/285
Vane kits to spread larger working widths |  | For 21m - includes only inclination indicator | For 27/28m - includes 4 x 285mm vanes & inclination indicator | For 27/28m - includes 4 x 285mm vanes & inclination indicator | 27 - 33 m includes 8 x 285mm vanes |  |  | 
Steel - straight HD (carbon hardened - KTL painted black) | STANDARD / OPTION |  |  |  | OPTION (only for 27-33m) | OPTION | OPTION | 
 | Length (mm) |  |  |  | 2 x 285/285/285 | 2 x 285/285/285 | 2 x 285/285/285 | 
Duplex (hardened stainless steel) - Lift vanes | STANDARD / OPTION |  |  |  |  | OPTION | OPTION | OPTION
 | Length (mm) |  |  |  |  | 2 x 330-5°/330-10°/330-10° | 2 x 330-5°/330-10°/330-10° | 2 x 230-5°/330-5°/330-10°/330-10°
Duplex (hardened stainless steel) - Lift vanes - HD (carbide coated) | STANDARD / OPTION |  |  |  |  | OPTION | OPTION | OPTION
 | Length (mm) |  |  |  |  | 2 x 330-5°/330-10°/330-10° | 2 x 330-5°/330-10°/330-10° | 2 x 230-5°/330-5°/330-10°/330-10°
Vanes model
Spreader model

## Slide 169
Gear Box RO-XL, RO-M GEOSPREAD®, RO-EDW and RO-XXL GEOSPREAD®
Centre gear box with 2 input shafts for high and low disc speed settings
Drive line with 2 rubber couplings

## Slide 170
1 rim RO-M/RO-M EW = 450 ltr (maximum 2 extensions)
1 rim RO-M GEOSPREAD® = 450 or 500 ltr (maximum 3 extensions)
1 rim RO-XL/RO-EDW/RO-EDW/ = 650 ltr or 675 ltr (maximum 3 extensions)
RO-XXL/GEOSPREAD®
Aluminum Extension Rims (Optional)

## Slide 171
Hopper Windows
Hopper windows at the top and the bottom of the hopper
Windows at the bottom of the hopper can be easily replaced by a hopper emptying kit
Quickly checked if hopper is almost empty, even with a hopper cover fitted on the spreader

## Slide 172
Fine application for RO-C is optional
Standard on:
RO-M, RO-M EW, RO-M GEOSPREAD®, RO-XL, RO-EDW and RO-XXL GEOSPREAD®
Fine Application Device

## Slide 173
How to Adjust the Fine Application Device?
Movie

## Slide 174
Agitator
RO-M/RO-M EW
RO-M GEOSPREAD®/RO-XL/
RO-EDW/RO-XXL GEOSPREAD®
RO-C
Agitator speed
=
Disc speed
540 rpm
Agitator speed
=
Disc speed
850 rpm
Agitator speed
=
15 % of the disc
speed

## Slide 175
Front part easy to open for quick inspection
Wide filling opening
Quick and simple to fit
Hopper Cover (Optional)

## Slide 176
Operation of electrical hopper cover via ISOBUS compatible terminal
No need to leave the tractor cab
Unique patented design
Electrical Hopper Cover

## Slide 177
Open/Close Indicator
Standard on all hydraulic models

## Slide 178
Delta Shaped Grids
1
2
3
1
2
3
Delta shaped heavy duty grids, big filling surface for a good flow, lumps are rolling down to avoid blocking of the grid.
Locked by grids in working position
Hand grip for easy and save opening and closing
Locked when the grid is open to avoid falling down or damaging the hopper edge

## Slide 179
Standard Heavy Duty Grids on all Models
All lumps will go to the edge of the rim, means constant big surface

## Slide 180
Accessory for RO-XL, RO-EDW and RO-EDW (GEOSPREAD®)
For spreading organic fertiliser
Special sieve with pattern of holes for a better flow in the hopper of the pellets.
Pellet Sieves

## Slide 181
Optional available for hydraulic models to open L and R independent from each other
Left/Right Independent Closing

## Slide 182
Calibration Test
Calibration container is optional available for all RO spreaders
Dismount the vanes
Disconnect the driveline
Fit calibration container

## Slide 183
Two bottom windows can easily be replaced by a hopper emptying kit
Easy to return a rest volume from the hopper into a storage
Hopper Emptying Kit

## Slide 184
Optional available for RO-M, RO-M EW, RO-XL, RO-EDW and RO-XXL GEOSPREAD®
Two positions possible:
  Transport position
  Working position
Ladder Set

## Slide 185
Foldable Side Step
Optional available on the RO-M GEOSPREAD® / RO-EDW / RO-XXL (GEOSPREAD®)
Can be assembled on both sides of the hopper

## Slide 186
A trailer is optional available for the RO-M GEOSPREAD®, RO-XL and RO-EDW GEOSPREAD® models
Max. 3 extension rims
Depending on country homologation
Trailer

## Slide 187
LED Lighting
LED lights are optional for the RO-C, RO-M, RO-M EW and RO-M GEOSPREAD®
LED lights are standard equipment for the RO-XL, RO-EDW and RO-XXL GEOSPREAD®.

## Slide 188
Mudguards
Mudguards are optional available for the RO-M GEOSPREAD®, RO-XL, RO-EDW and RO-XXL GEOSPREAD®
To protect the spreading disc against mud, water etc.

## Slide 189
Tramline Cylinder (RO-C/RO-M)
Available for RO-C and RO-M only
Hydraulically operated from tractor cab

## Slide 190
Border Spreading Plate (Manual)
Drive line can be disconnected for border spreading or a calibration test
Eco position
Environmental position

## Slide 191
Border Spreading Plate (Hydraulic)
Hydraulic operation of the border spreading plate possible from the tractor cab
Available for all models, except RO-C

## Slide 192
TrimFlow Border Spreading System
Right hand side version available for:
Available for RO-M, RO-M EW, RO-M GEOSPREAD®, RO-XL, RO-EDW and RO-XXL GEOSPREAD®
Operated hydraulically from tractor cab
Also as left hand version available for:
RO-XL, RO-EDW, RO-XXL GEOSPREAD®

## Slide 193
TrimFlow
Yield setting
ECO setting
H20 setting
H20 setting 0m
Yield setting 2m
Two sided
Border spreading plate

## Slide 194
Border Spreading Indicator (BSI)
Compulsory accessory in combination with the one of hydraulic border spreading devices. Hydraulic central border spreading plate or TrimFlow border deflector.
Indicates which border spreading device is active (transport or working position)
On weighing spreaders with EDW2 electronic only compulsory when more then 1 border spreading device is mounted.

## Slide 195
Central Hydraulic Drive
Spreading without a PTO-shaft
Available for the RO-XL / RO-EDW / RO-EDW GEOSPREAD®

## Slide 196
The RotaFlow spreading system: prevents fragmentation of the granules due to impact with the vanes and maintains the spreading characteristics of the material.
FlowPilot: The compact ‘dashboard’ on each disc has considerably simplified accurate setting and adjustment of application rates.
The RO-M EW/RO-M GEOSPREAD® and RO-EDW, RO-XXL GEOSPREAD® are ISOBUS compatible as standard: simple plug and play possible.
Easy to assemble aluminum hopper extension rims (RO-M GEOSPREAD®, RO-M EW, RO-XL, RO-EDW, RO-XXL GEOSPREAD®)
The 4 Key TakeAways, RO Disc Spreaders
1
2
3
4