## Slide 1: Kverneland Exacta Disc Spreaders
Product Presentation 2023/2024
Arable Systems Division - Crop Care Equipment

## Slide 2: Kverneland Exacta Disc Spreaders

## Slide 3: Kverneland Spreaders - Product Story
Precision farming is at the core of what we do at Kverneland. And with us precision farming is not only about electronics, it is at the base of everything we do to achieve our goal: to provide you with a disc spreader that takes care of your business: optimise revenue, decrease costs and long-term improvement of your land.
The Kverneland disc spreader is the only spreader that allows users to quickly and easily optimise the spreader settings after the actual properties of each batch of fertiliser instead of the generic fertiliser properties that other spreaders use. This allows for a much more precise configuration of the Kverneland disc spreader and leads to a much more precise spreading pattern.
We have been listening to your input for years, so we understand your needs when taking care of your crops and your business.

## Slide 4: CONTENT to Find What You Need
Fertiliser story & setting
CentreFlow Spreading System
Easy Set
Spreader range
Weighing system
GEOSPREAD® System
Section Control
Border spreading
Control Systems
IsoMatch GEOCONTROL®
MULTIRATE (VRA)
Vanes & accessories
Front – rear spreader

## Slide 5: Spreader Competence Centre
“Accurate spreading starts here”

## Slide 6: Spreader Competence Centre
Accuracy starts here
Ultra-modern test facility
Highly advanced 3D test system and software set up
Gives a quick availability of spreading charts to set up your spreader in the most accurate way
Movie

## Slide 7: Kverneland Exacta Disc Spreaders
Importance of physical properties

## Slide 8: Physical Properties of Fertiliser
Distribution (granule size)
Density (kg/l)
Shape and surface
Grain strength

## Slide 9: Physical Properties of Fertiliser

## Slide 10: Influence on Distribution
Distribution
  < 2mm (very small = ‘dust’)
  > 4,75mm (very heavy = ‘grid’)
  Ideal = 80% in the middle compartment:
  2 – 4,75mm
  For bigger working widths the most granules should be in the compartment
  3,3 – 4,75mm
Always in combination with:
  Density
  Grain strength
  Temperature and humidity (weak granules)

## Slide 11: Fertiliser Analysis & Demo set
Fertiliser Analysis & demo Kit
How to setup your spreader correctly? With this kit you will be able to explain everything about the physical properties of fertiliser which are important to determine to get the most accurate spreading advice and spreading pattern.
Content of the kit
Booklet with background information
6 fertiliser samples
Shaker-box
Litre weight
Weighing scale
Order code | Description | 
A148503930 | Fertiliser Demo Case (including fertiliser samples) | 
Movie

## Slide 12: Influence on Density
Ideal situation is
  +/- 1 kg/l
  Light: more sensitive for wind influence
  Limitation of maximal spreading width
  Heavy: risk of crop damage

## Slide 13: Influence on Shape and Surface
Resistance
  ‘Slide’ along each other and through the dosing system
  ‘Roll’ on the vane
  ‘Fly’ in the sky
  Round and smooth: easy flow
Fertiliser properties and limitations
  Sharp-edged shape means a longer travel time on the vanes for wide settings
  To get a correct spreading pattern, also behind the spreader, a ‘small’ setting is needed (e.g. Kali), but for this reason a limitation in maximum working width is needed.

## Slide 14: Influence on Grain Strength
Soft granule is more sensitive for damages
Coating
Working width: gives energy to the granule
Every change of direction: additional impact and resistance
Additional resistance: also additional wearing
Rough surface: additional resistance

## Slide 15: Example of Influence on Distribution
Three times ‘the same’ fertiliser
  KAS 0-15-80-5 with correct settings
  KAS 10-30-60-0, but kept the same setting as for KAS 0-15-80-5
  KAS 15-55-30-0, but kept the same setting as for KAS 0-15-80-5

## Slide 16
CV= 8,5%
CV= 8,4%
CV= 5,4%
WW= 24m
WW= 33m
WW= 39m
KAS 0-15-80-5 with correct settings

## Slide 17
CV= 18,1%
CV= 15,9%
CV= 6,3%
WW= 24m
WW= 33m
WW= 39m
10-30-60-0
KAS 10-30-60-0, but kept same settings as KAS 0-15-80-5

## Slide 18
CV= 27,4%
CV= 20,4%
CV= 7,4%
WW= 24m
WW= 33m
WW= 39m
KAS 15-55-30-0 but kept same settings as KAS 0-15-80-5

## Slide 19: Conclusions from Those Spreading Patterns
Small distribution comes with the same setting less far (wide).
Due to this there is no fertiliser between the tramlines and there is not enough overlap.
How larger the working width, the bigger this effect is.
This does not always mean that it is not possible to spread smaller fertiliser on a specific working width; but that you need adjusted settings on a bigger working width to keep a good spreading pattern.
   on smaller working widths the deviation is smaller or ‘invisible’
   so on larger working widths the importance of selecting the correct distribution is getting more and more important.
Also when using GPS section control the spreading pattern and settings must be taken into account!

## Slide 20: The Exacta Checklist for Accurate Spreading
1 Select fertiliser type (shape)
2 Determine granule size and distribution
3 Determine litre weight (kg/l)

## Slide 21
Take your spreading charts book
or
Open www.kvernelandspreadingcharts.com
or
Open your Spreading charts app on your iPhone or Android phone (free download from App Store or Google Play)
Book
Web
App
Select Your Machine
1

## Slide 22: Enter the Field Settings
Book
Web
App
2

## Slide 23: Select Fertiliser Type
3

## Slide 24
3
Select Fertiliser Type

## Slide 25: Determine Granule Size and Distribution
Fill your granule size box with fertiliser
Turn it and shake it well
Determine the granule size and distribution
4

## Slide 26: How to Use the Shaker Box?

## Slide 27: Determine Litre Weight (Density)
What is the weight of exactly 1 litre?
5

## Slide 28: Determine Litre Weight (Density)
What is the weight of exactly 1 litre?
5

## Slide 29: How to Determine the Density?

## Slide 30: Fill in the Data in the App/web or Find Your Spreading Table in the Book
6
Granule distribution

## Slide 31: Fill in the Data in the App/web or Find Your Spreading Table in the Book
Fertiliser type
6

## Slide 32
6
Litre weight
Fill in the Data in the App/web or Find Your Spreading Table in the Book

## Slide 33: Find Your Fertiliser
7
If your brand is not in the overview, please find the fertiliser which is the closest to your characteristics.
Kverneland is always advising to set-up your spreader based on the physical properties of the fertiliser, not the brand!

## Slide 34: See Your Advised Settings and Adjust Your Spreader Correctly
8

## Slide 35: ...or use the AutosetApp on the IsoMatch Tellus (GO+)
Settings automatically done via the AutosetApp
Always the most up to date spreading charts online available via the IsoMatch Tellus PRO or Tellus GO+
Update via: - IsoMatch Wireless - Download on an USB stick
After the selection the settings are automatically send to the spreader
9
Use granule size box to determine distribution
Determine litre weight
Determinate fertiliser type

## Slide 36: AutosetApp
Most close to measured specific weight and granule size distribution
Proposal is marked in green
After sending: Initial values for opening position and theoretical flow at this position is adjusted and Letter setting is put from « P » to « K »

## Slide 37: Spreading Charts
Direct access to the most recent test results at: www.kvernelandspreadingcharts.com
Download the spreading chart application from the Google Play Store or App Store
AutosetApp on IsoMatch Tellus GO+ or PRO

## Slide 38: The CentreFlow Spreading System

## Slide 39
Central release point, smooth
acceleration and centrifugal force
accelerates fertiliser up to
disc speed before it reaches
the vane.
The CentreFlow Principle
1
No impact,
No fragmentation
No dust
2
Accurate
spreading pattern
Large 8 vane discs allow 9 to 54m spread widths. Double overlap spreading pattern gives unrivalled accuracy.
3
Minimal wind influence,
maximum tolerance
Flat discs.
Horizontal spreading pattern.
4
Consistent spreading
pattern
Double overlap spreading pattern.
5
Guaranteed accuracy
on slopes
The fertiliser always contacts the vanes at the same point, also on slopes, and travels the complete length of the vanes.

## Slide 40: The CentreFlow Principle
Central release point, smooth
acceleration and centrifugal force
accelerates fertiliser up to
disc speed before it reaches
the vane.
No impact,
No fragmentation
No dust
1

## Slide 41: The CentreFlow Principle
8 vs. 2 vanes |  |  |  | 
 | Kg/Ha | Discs | No. of vanes | kg/vane/ha
Competition | 400 | 2 | 2 | 100
Kverneland | 400 | 2 | 8 | 25
2
Accurate
spreading pattern
Large 8 vane discs allow 9 to 54m spread widths. Double overlap spreading pattern gives unrivalled accuracy.

## Slide 42: Quality of Distribution
In working width and driving direction
The most optimal lateral distribution in the market
Split into 16 sectors (2x8)
Very important by higher forward speed
1
2
3
4
5
7
6
8
Optimal distribution with 8 vanes per disc
at higher speeds

## Slide 43: The CentreFlow Principle
3
Minimal wind influence,
maximum tolerance
Flat discs.
Horizontal spreading pattern.

## Slide 44: The CentreFlow Principle
Above 24 metre
36 m
24 m
Till 24 metre
4
Double overlap
Trapezium overlap
Trapezium
spread pattern with spreader
under an angle
48 m

## Slide 45: The CentreFlow Principle
5
Guaranteed accuracy on slopes
The fertiliser always contacts the vanes at the same point, also on slopes, and travels the complete length of the vanes.
Kverneland Exacta
Other brands

## Slide 46: EasySet
Easy Setting and Adjustment

## Slide 47: EasySet System
EasySet system
CL / HL
Fine application rate setting
Discharge point
Application rate setting
CL / CL-E / CL W PRO / CL-EW / HL / HL-E / TL / TLX (GEOSPREAD) / iDC
CL / CL-E / CL W PRO / CL EW / HL / HL-E / TL / TLX (GEOSPREAD) / iDC
CL / CL-E / CL W PRO / CL-EW / HL / HL-E / TL / TLX (GEOSPREAD) / iDC

## Slide 48: Adjustment Exacta Spreaders
Exacta CL / HL
Exacta CL-E / CL W PRO / CL-EW /
HL-E / TL
Exacta GEOSPREAD®
Exacta EL
1 electric actuator for application rate
2 electric actuators for application rate and discharge point

## Slide 49: Spreader Settings Exacta-EL
Discharge point
Application rate

## Slide 50: How to Adjust your Exacta-EL?

## Slide 51: Spreader Settings Exacta-CL
Discharge point
Application rate
Fine application

## Slide 52: Spreader Settings Exacta-HL-E / CL-E / CL-EW
Discharge point
Fine application

## Slide 53: How to Adjust your Exacta HL-E/CL-E/CL-EW?

## Slide 54: Spreader Settings Exacta-HL
Discharge point
Application rate
Fine application

## Slide 55: Spreader Settings Exacta-TL & CL W PRO
Discharge point
Fine application
Application rate
Automatic adjustment of:

## Slide 56: How to Adjust the Settings of a Weighing Spreader via an ISOBUS Terminal?

## Slide 57
How to Adjust the Settings of a Weighing Spreader via an IsoMatch Tellus Terminal?

## Slide 58: Spreader settings Exacta-CL, TL and TLX GEOSPREAD®
Discharge point
Fine application
Application rate
Automatic adjustment of:

## Slide 59: How to Adjust the GEOSPREAD® Spreader Settings via an ISOBUS Terminal?
Movie

## Slide 60: How to Adjust the GEOSPREAD® Spreader Settings via an IsoMatch Tellus Terminal?

## Slide 61: Kverneland Disc Spreader Range
Movie

## Slide 62: Kverneland Disc Spreader Range
Movie
NEXT NEWS

## Slide 63: Kverneland Exacta-EL

## Slide 64: Kverneland Exacta-EL
Overview
 | EL 700 | EL 900 | EL 1400
Hopper capacity (l) | 700 | 900 | 1400
Filling height (cm) | 96 | 108 | 128
Width (cm) | 154 | 154 | 176
Filling width (cm) | 148 | 148 | 170
Empty weight (kg) | 250 | 270 | 290
Spread width (m) | 9-18 (20/21)* | 9-18 (20/21)* | 9-18 (20/21)*
Output (kg/min) | 10-230 | 10-230 | 10-230
*with optional set of vanes
Kverneland Exacta-EL

## Slide 65
Three options of hopper capacity 700 – 900 – 1,400 litres
Four detachable vanes per disc determine the working width
CentreFlow spreading system
Hydraulic control

## Slide 66: Exacta-EL
Standard features
  Right hand spreading disc can be shut off
  Overload clutch
  Stainless steel hose connections
  Robust steel sieves
  Tool to open the sieve
  Grading box to test the fertiliser quality
  Four hopper windows
  All vanes for 9-18 m (4 vanes per disc)
  With longer vanes 21m working width is possible

## Slide 67: Kverneland Exacta-CL

## Slide 68: Kverneland Exacta-CL
Overview
*with optional set of vanes
 | CL 1100 | CL 1550 | CL 2000
Hopper capacity (l) | 1100 | 1550 | 2000
Filling height (cm) | 100 | 119 | 138
Width (cm) | 220 | 220 | 220
Filling width (cm) | 214 | 214 | 214
Empty weight (kg) | 325 | 350 | 375
Spread width (m) | 10-24 (27/28)* | 10-24 (27/28)* | 10-24 (27/28)*
Output (kg/min) | 10-320 | 10-320 | 10-320
Kverneland Exacta-CL

## Slide 69
Hydraulic control
Three options of hopper capacity
1100 – 1550 – 2000 litres
CentreFlow system
with 8 vanes per disc
EasySet: for accurate setting and adjustment of application rates
Easy to assemble aluminium hopper extensions
Set the right application rate and increase or decrease the application on the move
Both spreading discs can be shut off
independently to spread half the working width

## Slide 70: Exacta-CL
Standard features
  Integrated fine application facility
  Overload clutch
  Stainless steel hose connections
  2 Delta shaped heavy duty grids
  Tool to open the sieve
  Grading box to test the fertiliser quality
  Four hopper windows
  All vanes for 10-24 m
  With longer vanes 28m spreading width is possible

## Slide 71: Exacta-CL (Hydraulic)
Operation with double acting valve on tractor
Stainless steel hose connections
Application setting in 90 steps
Open/close indicator
CL E
CL

## Slide 72: Kverneland Exacta-HL

## Slide 73: Kverneland Exacta-HL 1500 – 2150 – 2800 – 3450
Overview
*with optional set of lift vanes
 | HL 1500 | HL 2150 | HL 2800 | HL 3450
Hopper capacity (l) | 1500 | 2150 | 2800 | 3450
Filling height (cm) | 110 | 129 | 148 | 167
Width (cm) | 275 | 275 | 275 | 275
Filling width (cm) | 269 | 269 | 269 | 269
Empty weight (kg) | 495 | 525 | 555 | 585
Spread width (m) | 12-54* | 12-54* | 12-54* | 12-54*
Output (kg/min) | 10-320 | 10-320 | 10-320 | 10-320
Kverneland Exacta-HL 1500 – 2150 – 2800 – 3450

## Slide 74: Kverneland Exacta-HL 1875 – 2550 – 3225 – 3900
Overview
*with optional set of lift vanes
 | HL 1875 | HL 2550 | HL 3225 | HL 3900
Hopper capacity (l) | 1875 | 2550 | 3225 | 3900
Filling height (cm) | 120 | 139 | 158 | 177
Width (cm) | 290 | 290 | 290 | 290
Filling width (cm) | 284 | 284 | 284 | 284
Empty weight (kg) | 530 | 565 | 595 | 625
Spread width (m) | 12-54* | 12-54* | 12-54* | 12-54*
Output (kg/min) | 10-320 | 10-320 | 10-320 | 10-320
Kverneland Exacta-HL 1875 – 2550 – 3225 – 3900

## Slide 75
Hydraulic control
Two options of basic hopper capacity 1500 or 1875 litres, can be extended with easy to assemble aluminium
hopper extension up to 3450 or 3900 litres
Slow rotating agitator
CentreFlow system
with 8 vanes per disc
EasySet: for accurate setting and adjustment of application rates
Long life time
LED lighting set

## Slide 76: Exacta-HL
Standard features
  Stainless steel front plates
  Fine application kit
  Overload clutch
  Stainless steel hose connections
  2 High capacity & robust sieves
  Tool to open the sieves
  Inclinometer
  Grading box to test the fertiliser quality
  Open/close indicator
  Top and bottom hopper windows
  Low speed agitator (15%)
  LED lighting set
Lift vanes
Standard vanes

## Slide 77: Exacta-HL (Hydraulic)
Operation with double acting valve on tractor
Stainless steel hose connections
Application setting in 90 steps
Open/close indicator
HL E
HL

## Slide 78: Kverneland Exacta-CL EW

## Slide 79: Kverneland Exacta-CL EW
Overview
*with optional set of vanes
 | CL EW 1100 | CL EW 1550 | CL EW 2000
Hopper capacity (l) | 1100 | 1550 | 2000
Filling height (cm) | 100 | 119 | 138
Width (cm) | 220 | 220 | 220
Filling width (cm) | 214 | 214 | 214
Empty weight (kg) | 380 | 400 | 425
Spread width (m) | 10-24 (27/28)* | 10-24 (27/28)* | 10-24 (27/28)*
Output (kg/min) | 10-320 | 10-320 | 10-320
Kverneland Exacta-CL EW

## Slide 80
Easy to assemble aluminium hopper extensions
Three options of hopper capacity
1100 – 1550 – 2000 litres
CentreFlow system
with 8 vanes per disc
One central 10 tonne load cell + reference sensor
AEF certified – ISOBUS compatible spreader
TC-SC ISOBUS Basic Section Control

## Slide 81: Exacta-CL EW
Standard features
  Best weighing results and dosing control
  Integrated weighing system
  1 central 10 ton load cell i.c.w. reference sensor
  Standard full ISOBUS compatible
  Compact design: gravity point stays close to tractor
  Four hopper windows
  Tool to open the sieve
  All vanes for 10-24 m
  With longer vanes 28m spreading width is possible
  SPREADERcontrol License option
  Basic Section Control
  4m section

## Slide 82: Kverneland Exacta-CL W PRO

## Slide 83: Kverneland CL W PRO* 1300-1800-2300-2800
Overview
 | CL W PRO 1300 | CL W PRO 1800 | CL W PRO 2300 | CL W PRO 2800
Hopper capacity (l) | 1300 | 1800 | 2300 | 2800
Filling height (cm) | 113 | 132 | 151 | 170
Width (cm) | 245 | 245 | 245 | 245
Filling width (cm) | 239 | 239 | 239 | 239
Empty weight (kg) | 496 | 521 | 547 | 573
Spread width (m) | 10-24 (27/33)* | 10-24 (27/33)* | 10-24 (27/33)* | 10-24 (27/33)*
Output (kg/min) | 10-320 | 10-320 | 10-320 | 10-320
*depending on type of fertiliser and type of vanes
NEXT NEWS
Kverneland CL W PRO 1300-1800-2300-2800

## Slide 84
Basic hopper capacity 1,300 litres, can be extended with easy to assemble aluminium hopper extensions up to 2800 litres
AEF certified –
ISOBUS compatible spreader
Slow rotating agitator
TC-SC ISOBUS
Basic Section Control - BSC
(4m sections)
CentreFlow system
with 8 vanes per disc
4 x 2,5 tonne load cells + reference sensor
NEXT NEWS
Movie

## Slide 85: Kverneland Exacta-TL

## Slide 86: Kverneland Exacta-TL 1500 – 2150 – 2800 – 3450
 | TL 1500 | TL 2150 | TL 2800 | TL 3450
Hopper capacity (l) | 1500 | 2150 | 2800 | 3450
Filling height (cm) | 110 | 129 | 148 | 167
Width (cm) | 275 | 275 | 275 | 275
Filling width (cm) | 269 | 269 | 269 | 269
Empty weight (kg) | 665 | 695 | 725 | 755
Spread width (m) | 12-54* | 12-54* | 12-54* | 12-54*
Output (kg/min) | 10-320 | 10-320 | 10-320 | 10-320
Overview
*with optional set of lift vanes

## Slide 87: Kverneland Exacta-TL 1875 – 2550 – 3225 – 3900
 | TL 1875 | TL 2550 | TL 3225 | TL 3900
Hopper capacity (l) | 1875 | 2550 | 3225 | 3900
Filling height (cm) | 120 | 139 | 158 | 177
Width (cm) | 290 | 290 | 290 | 290
Filling width (cm) | 284 | 284 | 284 | 284
Empty weight (kg) | 705 | 735 | 765 | 795
Spread width (m) | 12-54* | 12-54* | 12-54* | 12-54*
Output (kg/min) | 10-320 | 10-320 | 10-320 | 10-320
*with optional set of lift vanes
Overview
Kverneland Exacta-TL 1875 – 2550 – 3225 – 3900

## Slide 88
Long life time
LED lighting set
CentreFlow system with 8 vanes per disc
Two options of basic hopper capacity 1500 or 1875 litres, can be extended with easy to assemble aluminium hopper extensions
AEF certified – ISOBUS
compatible spreader
TC-SC ISOBUS Basic Section Control -BSC (4m sections)

## Slide 89: Exacta-TL
Standard features
  Constant weighing of the output
  ISOBUS compatible
  Stainless steel front plates
  Fine application kit
  Overload clutch
  Tool to open the sieve
  Inclinometer
  Stainless steel hose connections
  2 High capacity & robust sieves
  Grading box to test the fertiliser quality
  Top and bottom hopper windows
  Low speed agitator (15%)
  LED lighting set
  SPREADERcontrol License option:
  Basic Section Control (BSC)
  4m sections
Lift vanes
Standard vanes

## Slide 90: Spreader Update 2023-24
Prepared for the future:
G3 new generation of electronic on all GEOSPREAD spreader models
  Faster processor speed and need on the high spec machines
Diagnostic plug added
  Easier diagnostic & software flashing – direct connection of PCB G3 to TopService
New software with new User Interface (UI)
GEOSPREAD G3 electronics
NEXT NEWS

## Slide 91: Kverneland Exacta-CL GEOSPREAD®

## Slide 92: Kverneland CL GEOSPREAD® 1100-1550-2000-2450
Overview
 | CL GEOSPREAD 1100 | CL GEOSPREAD 1550 | CL GEOSPREAD 2000 | CL GEOSPREAD 2450
Hopper capacity (l) | 1100 | 1550 | 2000 | 2450
Filling height (cm) | 108 | 127 | 146 | 165
Width (cm) | 220 | 220 | 220 | 220
Filling width (cm) | 214 | 214 | 214 | 214
Empty weight (kg) | 483 | 506 | 529 | 552
Spread width (m) | 10-24 (27/33)* | 10-24 (27/33)* | 10-24 (27/33)* | 10-24 (27/33)*
Output (kg/min) | 10-320 | 10-320 | 10-320 | 10-320
*depending on type of fertiliser and type of vanes
Kverneland CL GEOSPREAD® 1100-1550-2000-2450

## Slide 93: Kverneland CL GEOSPREAD ® 1300-1800-2300-2800
Overview
 | CL GEOSPREAD 1300 | CL GEOSPREAD 1800 | CL GEOSPREAD 2300 | CL GEOSPREAD2800
Hopper capacity (l) | 1300 | 1800 | 2300 | 2800
Filling height (cm) | 113 | 132 | 151 | 170
Width (cm) | 245 | 245 | 245 | 245
Filling width (cm) | 239 | 239 | 239 | 239
Empty weight (kg) | 496 | 521 | 547 | 573
Spread width (m) | 10-24 (27/33)* | 10-24 (27/33)* | 10-24 (27/33)* | 10-24 (27/33)*
Output (kg/min) | 10-320 | 10-320 | 10-320 | 10-320
*depending on type of fertiliser and type of vanes
Kverneland CL GEOSPREAD ® 1300-1800-2300-2800

## Slide 94
Two options of basic hopper capacity 1,100 or 1,300 litres, can be extended with easy to assemble aluminium hopper extensions
AEF certified –
ISOBUS compatible spreader
Slow rotating agitator
GEOSPREAD®: Two actuators to control the discharge point and application rate
CentreFlow system
with 8 vanes per disc
4 x 2,5 tonne load cells + reference sensor

## Slide 95: Kverneland Exacta-TL GEOSPREAD®

## Slide 96
Kverneland TL GEOSPREAD® 1500-2150-2800-3450
 | Exacta-TL GEOSPREAD 1500 | Exacta-TL GEOSPREAD 2150 | Exacta-TL GEOSPREAD 2800 | Exacta-TL GEOSPREAD 3450
Hopper capacity (l) | 1500 | 2150 | 2800 | 3450
Filling height (cm) | 123 | 142 | 161 | 180
Width (cm) | 275 | 275 | 275 | 275
Filling width (cm) | 269 | 269 | 269 | 269
Empty weight (kg) | 655 | 685 | 715 | 745
Spread width (m) | 12-54* | 12-54* | 12-54* | 12-54*
Output (kg/min) | 10-320 | 10-320 | 10-320 | 10-320
*depending on type of fertiliser and vanes
Movie
Overview

## Slide 97
Kverneland TL GEOSPREAD® 1875-2550-3225-3900
 | Exacta-TL GEOSPREAD 1875 | Exacta-TL GEOSPREAD 2550 | Exacta-TL GEOSPREAD 3225 | Exacta-TL GEOSPREAD 3900
Hopper capacity (l) | 1875 | 2550 | 3225 | 3900
Filling height (cm) | 123 | 142 | 161 | 180
Width (cm) | 290 | 290 | 290 | 290
Filling width (cm) | 284 | 284 | 284 | 284
Empty weight (kg) | 695 | 725 | 755 | 785
Spread width (m) | 12-54* | 12-54* | 12-54* | 12-54*
Output (kg/min) | 10-320 | 10-320 | 10-320 | 10-320
*depending on type of fertiliser and vanes
Overview
Overview

## Slide 98
Two options of basic hopper capacity 1500 or 1875 litres, can be extended with easy to assemble aluminium hopper extensions
AEF certified – ISOBUS compatible spreader
CentreFlow system with 8 vanes per disc
GEOSPREAD®: Two actuators to control the discharge point and application rate
4 x 5 tonne load cell
+ reference sensor
TC-SC ISOBUS section control (1m sections)
TC-GEO VRA & MULTIRATE

## Slide 99: Kverneland Exacta-TLX GEOSPREAD®

## Slide 100
Kverneland TLX GEOSPREAD® 1875-2550-3225-3900
 | Exacta-TLX GEOSPREAD 1875 | Exacta-TLX GEOSPREAD 2550 | Exacta-TLX GEOSPREAD 3225 | Exacta-TLX GEOSPREAD 3900
Hopper capacity (l) | 1875 | 2550 | 3225 | 3900
Filling height (cm) | 123 | 142 | 161 | 180
Width (cm) | 290 | 290 | 290 | 290
Filling width (cm) | 284 | 284 | 284 | 284
Empty weight (kg) | 705 | 735 | 765 | 795
Spread width (m) | 24-45* | 24-45* | 24-45* | 24-45*
Output (kg/min) | 10-540 | 10-540 | 10-540 | 10-540
*depending on type of fertiliser and vanes
Overview
Movie

## Slide 101
Four options of hopper capacity
1875 – 2550 – 3225 – 3900 litres
AEF certified – ISOBUS compatible spreader
High speed (flow) CentreFlow system with 8 vanes per disc
GEOSPREAD®: Two actuators to control the discharge point and application rate
TC-SC ISOBUS section control (1m sections)
TC-GEO VRA & MULTIRATE
4 x 5 tonne load cell
+ reference sensor

## Slide 102: Kverneland TLX GEOSPREAD®
High speed spreading under all circumstances.
Newly designed CentreFlow system with 8 high capacity vanes on each disc for a perfect overlap, no matter how fast you are driving.

## Slide 103: Kverneland Exacta-TL and TLX GEOSPREAD iDC®

## Slide 104
Kverneland TL GEOSPREAD® iDC 1875-2550-3225-3900
 | TL GEOSPREAD iDC 1875 | TL GEOSPREAD iDC 2550 | TL GEOSPREAD iDC 3225 | TL GEOSPREAD iDC 3900
Hopper capacity (l) | 1875 | 2550 | 3225 | 3900
Filling height (cm) | 119 | 138 | 157 | 176
Width (cm) | 290 | 290 | 290 | 290
Filling width (cm) | 284 | 284 | 284 | 284
Empty weight (kg) | 700 | 730 | 760 | 790
Spread width (m) | 12-54* | 12-54* | 12-54* | 12-54*
Output (kg/min) | 10-320 | 10-320 | 10-320 | 10-320
Overview
*depending on type of fertiliser and type of vanes
NEXT NEWS

## Slide 105
Kverneland TLX GEOSPREAD® iDC 1875-2550-3225-3900
 | TLX GEOSPREAD iDC 1875 | TLX GEOSPREAD iDC 2550 | TLX GEOSPREAD iDC 3225 | TLX GEOSPREAD iDC 3900
Hopper capacity (l) | 1875 | 2550 | 3225 | 3900
Filling height (cm) | 122 | 141 | 160 | 179
Width (cm) | 290 | 290 | 290 | 290
Filling width (cm) | 284 | 284 | 284 | 284
Empty weight (kg) | 710 | 740 | 770 | 800
Spread width (m) | 12-45* | 12-45* | 12-45* | 12-45*
Output (kg/min) | 10-540 | 10-540 | 10-540 | 10-540
Overview
NEXT NEWS
Overview
*depending on type of fertiliser and type of vanes

## Slide 106: Kverneland TL & TLX GEOSPREAD® iDC
Four options of hopper capacity
1875 – 2550 – 3225 – 3900 litres
AEF certified - ISOBUS compatible spreader
High speed CentreFlow system with 8 vanes per disc
GEOSPREAD®: Two actuators to control the discharge point and application rate
Working width: TL GEOSPREAD iDC up to 54m TLX GEOSPREAD iDC up to 45m
Hydraulic drive with independent disc speed (L/R)
Four load cells and reference sensor
NEXT NEWS

## Slide 107: Kverneland GEOSPREAD® System
CL W PRO/ CL GEOSPREAD / TL / TL GEOSPREAD (iDC) / TLX GEOSPREAD (iDC)

## Slide 108: Four Weigh Cells Principle CL W PRO/ CL GEOGEOSPREAD / TL / TL GEOSPREAD (iDC) / TLX GEOSPREAD (iDC)
Reference sensor
5,0 ton load cell - TL
2,5 ton load cell -
5,0 ton load cell - TL
2,5 ton load cell -
5,0 ton load cell - TL
2,5 ton load cell -
5,0 ton load cell - TL
2,5 ton load cell -

## Slide 109: Continuous Weighing with Kverneland
Signal from the load cells
Signal from the reference sensor
Automatic correction of shocks
Kverneland’s reference sensor technology: all negative influences (shocks, bouncing, speeding up / slowing down, inclination) are corrected and eliminated, ensuring utmost spreading accuracy in all conditions.
Continuous dynamic ‘online – calibration’ with high frequency communication signal.

## Slide 110: Continuous Weighing with Kverneland
Load cells in combination with the reference sensor
Auto calibrating and continuous weighing system
Automatic correction on slopes
Automatic correction of shocks, even on rough terrain
Automatic speed related dosing system
No calibration test needed
Accurate weighing during spreading NON-STOP
Technology of 21st century
Weighing system is not influenced in hilly conditions, speed change
Possible continues auto calibration
Increasing accuracy in every conditions
Eliminating influence of changing fertiliser properties
Exact documentation how much you spread
Online control

## Slide 111: GEOSPREAD® System
Standard features
Additional 2 actuators on each spreading disc
GPS section control in minimum 1m wide sections
Movie

## Slide 112: GEOSPREAD® System
Two actuators on each dosing unit
  one controls the discharge point (sections)
  second controls the application rate (fertilifer flow)
Adjust letter setting individually from the tractor cab (automatically from AutosetApp)
Automatic start/stop with GPS on head lands possible
TC-SC ISOBUS section control
TC-GEO variable rate applications (VRA)

## Slide 113: IsoMatch GEOCONTROL® in Combination with GEOSPREAD®
Working width will be automatically adjusted to suit the overlap and coverage using a GPS positioning system
GEOSPREAD® is using the Section Control function of the IsoMatch GEOCONTROL® software which is in the IsoMatch Tellus GO+ or IsoMatch Tellus PRO terminal
Spreader working width is divided into a maximum of:
  CL GEOSPREAD® - 33* sections of 1 metre
  TL GEOSPREAD® (iDC) and TLX GEOSPREAD® (iDC) 54* sections of 1 metre
Not only the spreading width is adjusted, the application rate (kg/min) is also adjusted automatically to match the revised spreading width.
* max. number of sections always depends on the terminal task controller

## Slide 114: GPS Controlled Intelligent Machine Solutions
Full spreading width 24m with 24 sections*
*Using IsoMatch GEOCONTROL® in combination with all GEOSPREAD®

## Slide 115: GPS Controlled Intelligent Machine Solutions
Decreasing the spreading width on the right hand side by 3 m*
*Using IsoMatch GEOCONTROL® in combination with all GEOSPREAD®

## Slide 116: GPS Controlled Intelligent Machine Solutions
*Using IsoMatch GEOCONTROL® in combination with all GEOSPREAD®
Decreasing the spreading width on the left hand side by 5 m*

## Slide 117: GPS Controlled Intelligent Machine Solutions
Decreasing the spreading width of both sides by 4 m*
*Using IsoMatch GEOCONTROL® in combination with all GEOSPREAD®

## Slide 118: GPS Controlled Intelligent Machine Solutions
Switching the sections over the middle from one side*
*Using IsoMatch GEOCONTROL® in combination with CL GEOSPREAD®

## Slide 119: GEOSPREAD® Sections
Section control based on ISOBUS protocol
The CL GEOSPREAD® has maximum 33 sections, minimum 1m wide
The TL and TLX GEOSPREAD® (iDC) have maximum 54 sections, minimum 1m wide
Percentage of overlap adjustable from 0-100%
24 sections with No overlap 24 sections with Full overlap

## Slide 120: Advantages GEOSPREAD®
Quick and accurate spreading, with the discharge point being controlled by actuators.
The small 1 metre sections can be switched inside-out and outside-in to keep overlaps to the minimum.
Stable disc RPM in combination with discharge point adjustment maintains the spreading pattern.
Easy operation: no need to leave the tractor cab to adjust the working width
100% ISOBUS compatible for easy operation.

## Slide 121: GEOPOINT®
Measured in the Spreader Competence Centre.
The fertiliser type and spreader settings determine the GEOPOINT®, the point where fertiliser drops on the field.
The Centre of the 3D spreading pattern is used for optimum performance when opening and closing the dosing system on headlands.
The GEOPOINT® can be found in the spreading charts manuals or on the website and will be set automatically when using the AutosetApp.

## Slide 122: Automatic Section Control

## Slide 123: Types of Section Control
Examples with 24 metre working width

## Slide 124: Working Principle

## Slide 125: Performance of GEOSPREAD® and Basic Section Control

## Slide 126: Basic Section Control – Sections & Working Width Examples
CL-EW/CL W PRO
18 m 4m / 5m / 5m / 4m
20 m 4m / 6m / 6m / 4m
21 m 4m / 6.5m / 6.5m / 4m
CL-EW/CL W PRO
16 m 4m / 4m / 4m / 4m
Generation 2 electronics (EDW2) for spreader models CL EW, CL W PRO & TL

## Slide 127: Basic Section Control – Sections & Working Width Examples
CL-EW/CL W PRO
24 m 4m / 4m / 4m / 4m / 4m / 4m
CL-EW/CL W PRO
28 m 4m / 4m / 6m / 6m / 4m / 4m
Generation 2 electronics (EDW2) for spreader models CL EW, CL W PRO & TL

## Slide 128: Basic Section Control – Sections & Working Width Examples
CL-EW/CL W PRO
28m in combination with central border spreading plate, 8 sections are possible 4m / 4m / 4m / 2m / 2m / 4m / 4m / 4m
Generation 2 electronics (EDW2) for spreader models CL EW, CL W PRO & TL

## Slide 129
TL 54 m 12 + 2 in the middle in case of central border spreading plate is used
TL 48 m - 12 x 4 m
4m / 4m / 4m / 4m / 4m / 4m / 4m
Basic Section Control – Sections & Working Width Examples
Generation 2 electronics (EDW2) for spreader models CL EW, CL W PRO & TL

## Slide 130: Border Spreading

## Slide 131: Tramline Cylinder (Exacta EL / Exacta CL)
Available for Exacta-EL and CL only
Hydraulically operated from tractor cab

## Slide 132: Border Spreading Plate (Manual)
Available for all Exacta models
Drive line can be disconnected for border spreading or a calibration test

## Slide 133: Central Border Spreading Plate (Deflector)
Hydraulically controlled of the border spreading plate (deflector) possible from the tractor cab
Available for all models, except Exacta-EL

## Slide 134: ExactLine Border Spreading System
Left and right hand side version available for:
Exacta-CL, CL EW, CL W PRO, CL GEOSPREAD®, HL and TL, TLX GEOSPREAD® (iDC)
Operated hydraulically from tractor cab

## Slide 136: Border Spreading Indicator (BSI)
Compulsory accessory in combination with one of the hydraulic border spreading devices -> Hydraulic central border spreading plate or ExactLine border deflector.
Indicates which border spreading device is active (transport or working position)
On all standard weighing spreaders with G2 (EDW2) electronics (CL EW, CL W PRO & TL). Only compulsory when more then 1 border spreading device is assembled
BSI is NOT needed for G3 electronic with new UI  all GEOSPREAD® models
NEXT NEWS

## Slide 137: Border Spreading Indication (G3 Electronics)
BSI box NOT needed for G3 electronic new UI  all GEOSPREAD® models
Indication which border spreading device is active (transport or working position) directly on terminal screen
NEXT NEWS

## Slide 138: Control Systems

## Slide 139: Exacta CL-E / HL-E: Remote Control II
Application rate setting with control box
12 v power needed
Application rate setting
Central and L&R separate over/under dosing
Separate R/L and open/close, Field registration
Calibration program
NO speed controlled spreader
CL-E
CL

## Slide 140: All Our Weighing Spreaders are Standard ISOBUS Compatible

## Slide 141: ISOBUS Compatible Spreaders
International standard: plug and play functionality between terminal and spreader, when AEF certified!
Free Compatibility check via AEF Database
Supported Features:
UT | Universal Terminal | 
TECU | Tractor ECU | 
AUX-N | Auxiliary Control “NEW” | 
TC-BAS | Task Controller basic functionality | (ISO-XML data exchange, as applied totals, hr, kg, etc.)
TC-GEO* | Task Controller geo-based | (location data, Variable Rate application maps)
TC-SC** | Task Controller Section Control** | 
*/** may need a license activation code on both Terminal and/or implement

## Slide 142: Terminal & Spreader Functionality
Based on Licenses
Terminal |  | Spreader | 
 | License | None | SPREADERcontrol
iM Tellus (PRO) | None | UT, TC-BAS | UT, TC-BAS, TC-GEO TC-SC
 | GEOCONTROL | UT, TC-BAS, TC-GEO | UT, TC-BAS, TC-GEO TC-SC
iM Tellus GO+ | None | UT, TC-BAS, | UT, TC-BAS, TC-GEO TC-SC
 | GEO-VR | UT, TC-BAS, TC-GEO | UT, TC-BAS, TC-GEO
 | GEO-SC | UT, TC-BAS, TC-GEO | UT, TC-BAS, TC-GEO TC-SC
 | GEO-VR + GEO-SC | UT, TC-BAS, TC-GEO | UT, TC-BAS, TC-GEO TC-SC
Everything about ISOBUS and AEF: www.aef-online.org / www.aef-isobus-database.org

## Slide 143
1
2
ISOBUS Communication System
ISOBUS Communication System
ISOBUS tractor If the tractor already has an ISOBUS 11783 compatible terminal, there is no need for any additional terminal.
IsoMatch Tellus Pro For tractors with or without an ISOBUS 11783 terminal a IsoMatch Tellus terminal in combination with the necessary additional cables gives the possibility to operate all ISOBUS 11783 compliant implements from any manufacturer.
IsoMatch Tellus GO+ The IsoMatch Tellus GO+ is a Universal ISOBUS Terminal. This multifunctional one-screen terminal has been developed for fast and simple control of any ISOBUS implement, giving the farmer a ‘custom made’ experience as it suits all needs for simple and efficient handling of farming machinery and tasks.

## Slide 144: IsoMatch Tellus GO+
State of art: dual core processor
  Faster boot time (compared to IsoMatch Tellus GO)
  Faster response time (compared to IsoMatch Tellus GO)
  Capable of handling more and more demanding applications
Glossy display
Supporting IsoMatch Wireless
  Enabling Wi-Fi functionality
Ready to evolve with new functions, features and APP’s
  IsoMatch FarmCentre

## Slide 145: IsoMatch Tellus PRO Universal Terminal
Two ISOBUS interface screens
Large 12.1” colour touch screen
Intuitive operation
Basic DOC registration program to save operational information directly to USB
Four USB slots for easy data exchange, wireless USB stick or USB to serial cable
Built in PDF reader
RS232 connection for GPS receivers or sensors
Internet connection via a wireless USB stick or router
Integrated web browser
Ready to evolve with new functions, features and App’s
  IsoMatch FarmCentre

## Slide 146
Multi Functional Terminal
Camera
IsoMatch GEOCONTROL®
Touch screen
2 ISOBUS machines
PDF reader
Calculator

## Slide 147: IsoMatch GEOCONTROL® and IsoMatch Products

## Slide 148: IsoMatch GEOCONTROL®
Section control Automatic switching on and off implement sections on headlands, boundaries and already covered areas to minimise overlap

## Slide 149: IsoMatch GEOCONTROL®
Licenses IsoMatch Tellus GO+
In the IsoMatch Tellus GO+ this license key is divided in two parts, separate available from the IsoMatch Shop. Customers can buy just the functionality they need.
  IsoMatch GEO-SC  automatic section control
    Sector and headlands control distributed in up to 24 sections depending on the implement to which it is connected.
  IsoMatch GEO-VR  automatic variable rate control
    Variable rate control based on data provided by prescription maps or external sensors. Single channel in the entire working width.
  Working range is 2 km from starting point

## Slide 150: IsoMatch GEOCONTROL®
Licenses IsoMatch Tellus PRO
In the IsoMatch Tellus PRO there is 1 license key which is called IsoMatch GEOCONTROL®. It combines the 2 functionalities below
  Automatic Section Control
    Section and headlands control distributed in up to 88 sections depending on the implement to which it is connected.
  Automatic Variable Rate Control
    Variable rate control based on data provided by prescription maps or external sensors. Single channel in the entire working width.
  Working range is 10 km from starting point

## Slide 151: IsoMatch GEOCONTROL®
Documentation All documentation and data can be exchanged between farm management system and IsoMatch GEOCONTROL® via an USB stick.

## Slide 152: IsoMatch GEOCONTROL®
Advised driving position using guidance lines in the field and on headlands
Extendable using the optional IsoMatch InLine light bar, to place guidance in line of sight
Smart boundary recording: independent from the working width, even without any implement corrected
Boundary shrinking: create new inner boundaries by setting de desired width of the headland
Manual guidance for all operations
Manual guidance

## Slide 153: IsoMatch GEOCONTROL®
AutosetApp (included in IsoMatch GEOCONTROL® v1.9)
The most up to date setting for your weighing spreader are always online available
The AutosetApp connects the IsoMatch Tellus and IsoMatch Tellus GO+ terminal directly with the Kverneland weighing spreader and will automatically adjust the spreader according to the setting entered into the App.
Movie

## Slide 154: AutosetApp
Always the latest online spreading charts available via IsoMatch Tellus or IsoMatch Tellus GO+
Update by:
  IsoMatch wireless
  Download on USB memory stick
Forward the settings from the spreading chart to the spreader and adjust it automatically

## Slide 155: IsoMatch GEOCONTROL® - Brings Clear Benefits
Easy and comfort of operation, due to not having to manually switch on or off sections or change the application rate. You can focus 100% on the driving in the field.
More efficient work and avoiding overlap leads to cost savings of 5-10% on e.g. fertiliser.
With IsoMatch GEOCONTROL®, working at night time becomes very easy. IsoMatch GEOCONTROL® reduces the workload considerably.

## Slide 156
Spreading at Night!

## Slide 157: IsoMatch Global 3
IsoMatch Global 3 is a GPS antenna
It provides DGPS signal to the IsoMatch terminals with good level of accuracy pass to pass.
It works with satellite constellations L1 GPS, G1 GLONASS, E1 Galileo, and B1 BeiDou.

## Slide 158: IsoMatch Global 3
Technical specifications
DGPS accuracy
Simple installation on tractor roof. Magnetic support delivered with the standard package.
One single cable to connect to IsoMatch Terminals. Plug and Play functionality.
LED for signal status
  Blinking Red - Power on
  Blinking Amber - GNSS position available

## Slide 159: IsoMatch Eye
Working in the dark possible
View of 120°

## Slide 160: IsoMatch InLine
Distance to A-B line with LED indication and numeric display
Manual guidance in combination with IsoMatch GEOCONTROL®
Displays status of machine sections

## Slide 161: IsoMatch WireLess
Internet connection to any available wireless network
No additional costs from the internet service provider
Browsing on the spot
Only available in the EU/USA

## Slide 162: IsoMatch Grip
In combination with IsoMatch Tellus PRO or IsoMatch Tellus GO+
Up till 44 functions divided over 4 modes can be programmed to cover the spreading needs
Fully ISOBUS compatible

## Slide 163: IsoMatch FarmCentre
Data Flow
Dongle
WiFi or Mobile

## Slide 164: Benefits of IsoMatch FarmCentre
Always Connected
  With your device, stay fully up to date on what is happening on your farm
Wireless Transfer of Task Data
  Exchange of Taskdata with Farm Management System
  Planned tasks, Finished tasks
  Variable rate application maps
  Field boundaries
Documentation
  Increased efficiency as less time is spent on administrating tasks
  Service support
  Report alarms & notifications

## Slide 165: MULTIRATE

## Slide 166: IsoMatch GEOCONTROL®
Variable Rate Control
Automatically adjusts the implement application rate based on input from the field prescription
The IsoMatch Tellus PRO requires field maps in ISO-XML format
The task map is displayed in the IsoMatch GEOCONTROL® screen
To operate variable rate application with two or more rates a licence must be activated
Spreaders with software version 1.20 and higher support MULTIRATE
Needs to be checked ISBUS terminal is supporting MULTIRATE functionality
MULTIRATE control NOT SUITABLE i.c.w. IsoMatch Tellus GO+ !!!

## Slide 167: IsoMatch GEOCONTROL®
Example single rate
The input rate is determined at the GEOPOINT®. The value in the Variable Rate map provides a value of 170 kg/ha.
But the spreader covers area on the map with 150 kg/ha till 195 kg/ha input rate as well.
The deviation from the VRA map is -25 till +20 kg/ha.
The average deviation on the left disc is -21 kg/ha.
The average deviation and for the right disc +10 kg/ha.

## Slide 168: IsoMatch GEOCONTROL®
Example MULTIRATE 2 rates
The input rates are determined at the middle of the left and right of the spreader “boom”. The Variable Rate map provides different values of (190 vs 170 kg/ha) for the left and right disc.
The deviation from the VRA map is reduced to -5 till +20 kg/ha.
The average deviation for the left disc is reduced to -1,2 kg/ha and for the right disc to +10 kg/ha.

## Slide 169: IsoMatch GEOCONTROL®
Example MULTIRATE 8 rates
The input rates are determined at 8 points at the spreader “boom”. The VRA map provides different values of (192 vs 160 kg/ha) for the left and right disc.
The deviation from the VRA map is reduced to -10 till +10 kg/ha.
The average deviation for the left disc is reduced to +0,8 kg/ha and for the right disc to +0 kg/ha.

## Slide 170: Others – Vanes & Accessories

## Slide 171: Standard Range of Vanes (Straight)
Exacta-EL
Exacta-CL / CL-EW

## Slide 172: Standard Range of Vanes (Straight)
Exacta-CL W PRO / CL GEOSPREAD
Exacta-HL / TL / TL GEOSPREAD (iDC)

## Slide 173: Standard Range of Vanes (Straight)
Exacta-TLX GEOSPREAD (iDC)
85 3 3/8"

## Slide 174: Optional Range of Vanes (HD Straight)
Exacta-HL / TL / TL/TLX GEOSPREAD (iDC)
HD carbon hardened - KTL painted black

## Slide 175: Lift Vanes
  For spreading width up to 54m
  Spreading Urea up to 36m
  Only dedicated spreading tables
  DUPLEX Stainless steel
  Only for HL/TL/TLX/ GEOSPREAD®
  Possible in combination with ExactLine border spreading system

## Slide 176: Heavy Duty Vanes (Coated)
  More wear resistant (Tungsten carbide) lift vanes for Exacta-HL/TL/TL/TLX (GEOSPREAD)
  For hard granules, high flow (rate & working width) i.c.w. a lot of hectares
Heavy Duty Vanes (Hardened)
  More wear resistant (carbonised - hardened) straight vanes for HL/TL/TL (GEOSPREAD)
  For hard granules and high flow (rate & working width) i.c.w. a lot of hectares

## Slide 177: Optional Range of Vanes (Lift Vanes)
Exacta-HL / TL / TL GEOSPREAD (iDC)
Duplex or HD (carbide coated)
330 13 "

## Slide 178: Optional Range of Vanes (Lift Vanes)
Exacta-TLX GEOSPREAD (iDC)
Duplex or HD (carbide coated)
330 13 "
230 9 1/16"

## Slide 179: Range of Vanes - Total Overview
 |  | EL | CL | CL-EW | CL W PRO/CL GEOSPREAD | HL | TL/TL GEOSPREAD (iDC) | TLX GEOSPREAD (iDC)
Stainless Steel - straight | STANDARD / OPTION | STANDARD | STANDARD | STANDARD | STANDARD | STANDARD | STANDARD | STANDARD
 | Length (mm) | 2 x 135/185/235 | 2 x 135/185/235/285 | 2 x 135/185/235/285 | 2 x 135/185/235/285 | 2 x 285/285/285 | 2 x 285/285/285 | 2 x 85/285/285/285
Vane kits to spread larger working widths |  | For 21m - includes only inclination indicator | For 27/28m - includes 4 x 285mm vanes & inclination indicator | For 27/28m - includes 4 x 285mm vanes & inclination indicator | 27 - 33 m includes 8 x 285mm vanes |  |  | 
Steel - straight HD (carbon hardened - KTL painted black) | STANDARD / OPTION |  |  |  | OPTION (only for 27-33m) | OPTION | OPTION | 
 | Length (mm) |  |  |  | 2 x 285/285/285 | 2 x 285/285/285 | 2 x 285/285/285 | 
Duplex (hardened stainless steel) - Lift vanes | STANDARD / OPTION |  |  |  |  | OPTION | OPTION | OPTION
 | Length (mm) |  |  |  |  | 2 x 330-5°/330-10°/330-10° | 2 x 330-5°/330-10°/330-10° | 2 x 230-5°/330-5°/330-10°/330-10°
Duplex (hardened stainless steel) - Lift vanes - HD (carbide coated) | STANDARD / OPTION |  |  |  |  | OPTION | OPTION | OPTION
 | Length (mm) |  |  |  |  | 2 x 330-5°/330-10°/330-10° | 2 x 330-5°/330-10°/330-10° | 2 x 230-5°/330-5°/330-10°/330-10°
Vanes model
Spreader model

## Slide 180: Gear Box HL, CL GEOSPREAD, TL & TLX GEOSPREAD® (iDC)
Centre gear box with 2 input shafts for high and low disc speed settings
Drive line with 2 rubber couplings

## Slide 181: Aluminium Hopper Extensions (Optional)
1 rim CL/CL EW = 450 ltr (maximum 2 extensions)
1 rim CL GEOSPREAD® = 450 or 500 ltr (maximum 3 extensions)
1 rim CL W PRO = 500 ltr (maximum 3 extensions)
1 rim HL/TL/TLX/GEOSPREAD® = 650 ltr or 675 ltr (maximum 3 extensions)
1 rim TL/TLX/GEOSPREAD® (iDC) = 675 ltr (maximum 3 extensions)

## Slide 182: Hopper Windows
Hopper windows at the top and the bottom of the hopper
Windows at the bottom of the hopper can be easily replaced by a hopper emptying kit
Quickly checked if hopper is almost empty, even with a hopper cover fitted on the spreader

## Slide 183: Fine Application Device
Exacta-CL, CL EW, CL W PRO, CL GEOSPREAD®, HL and TL, TLX GEOSPREAD® (iDC) are standard equipped with a fine application device
Optional available for Exacta EL

## Slide 184: How to Adjust the Fine Application Device?

## Slide 185: Agitator
EL
CL/CL EW
CL W PRO, CL GEOSPREAD, HL/TL/TLX/GEOSPREAD (iDC)
Agitator speed
=
Disc speed
540 rpm
Agitator speed
=
Disc speed
850 rpm
Agitator speed
=
15 % of the disc speed

## Slide 186: Hopper Cover (Optional)
Easy to make a wide filling opening
Quick and easy to fit

## Slide 187: Electrical Hopper Cover
Operation of electrical hopper cover via ISOBUS compatible terminal
No need to leave the tractor cab
atented design
Folding mechanism and electric motor
Outside of hopper

## Slide 188: Open/Close Indicator
Standard on all hydraulically controlled spreader models

## Slide 189: Delta Shaped Grids
1
Locked grids in working position
Hand grip for easy and save opening and closing
Lock when the grid is open to avoid falling down or damaging
the hopper edge
2
3
1
2
3

## Slide 190: Standard Heavy Duty Grids on all Models
All lumps will go to the edge of the rim, means constant big surface

## Slide 191: Pellet Sieves
Accessory for Exacta-HL, TL and TLX (GEOSPREAD®)
For spreading organic fertiliser e.g. pellets
Special sieve with pattern of holes for a better flow in the hopper of the pellets.

## Slide 192: Left / Right Independent Closing
Optional available for hydraulically controlled models to open L and R independent from each other

## Slide 193: Calibration Test
Calibration container is optional available for all Exacta spreaders
Dismount the vanes
Disconnect the driveline
Fit calibration container

## Slide 194: Hopper Emptying Kit
Two bottom windows can easily be replaced by a hopper emptying kit
Easy to return a rest volume from the hopper into a storage

## Slide 195: Ladder Set
Optional available for Exacta-CL, CL EW, HL,TL and TLX GEOSPREAD®
Two positions possible:
  Transport position
  Working position

## Slide 196: Foldable Side Step
Optional available on the Exacta- CL W PRO, CL GEOSPREAD® + TL, TL/TLX GEOSPREAD® (iDC)
Can be assembled on both sides of the hopper

## Slide 197: Trailer
Trailer available for:
  Exacta-HL /TL (GEOSPREAD): max. 3 extension rims
  Depending on country homologation!

## Slide 198: LED Lighting
LED lights are optional for the Exacta-EL, CL, CL-EW, CL W PRO & CL GEOSPREAD®
LED lights are standard equipment for the Exacta-HL, TL and TLX GEOSPREAD® (iDC)

## Slide 199: Mudguards
To protect the spreading disc against mud, water etc.
Mudguards are optional available for:
Exacta- CL W PRO & CL GEOSPREAD®
Exacta-HL, TL and TL/TLX GEOSPREAD® (iDC)

## Slide 200: Front-Rear Spreader Combination

## Slide 201: Front Mounted Disc Spreader
Increase capacity with the combination of a rear mounted spreader (up to 5000I, 6000l over even 7000l)
A higher working speed is possible compared to a trailed spreader
Better spreading pattern: no need to spread blended fertiliser (split dependent on fertiliser properties  higher nutrition distribution accuracy)
Cost savings in time and labour
Possible combination for One-Pass technologies

## Slide 202: Front Mounted Disc Spreader
Short time frame in season for spreading fertiliser, which requires a high capacity and high speed spreader: not enough spreading capacity fits to “agronomic window”!
Weight balance/distribution of a big rear spreader on the tractor is not good, ground pressure/soil compaction especially in spring, wet conditions is a big problem for the soil!
Several passes in wet conditions destroy the soil structure: need to combine much different fertiliser types  mix of granules is not compatible for a good spreading quality.
Blended fertilisers  Bad accuracy of nutrition distribution, because of different spreading patterns, due to different fertiliser properties (granule size/shape & density l/kg). Also a risk of separations of blend fractions in the hopper and a different flow. Blend is also not an ideal solution for VRA / MULTIRATE applications.

## Slide 203: Front Mounted Disc Spreader
Examples
Possible combinations of using different products in the front and rear spreader:
Different fertiliser in the front and rear (two different variable applications in one pass)
Fertiliser and slug pellets
Fertiliser and seeds (e.g. in cover crops)
In case of two different cover crops in one field, with a different request of properties (e.g. oilseed rape, peas, grass seed cereals, alfalfa, clover)
…. anything else?
Other machine combinations with a front spreader
Seeds (cover crop) i.c.w. seedbed harrows, comb/finger harrows
Fertiliser i.c.w. any cultivator e.g. stubble, seedbed, comp/finger harrows
… what else?

## Slide 204: The 4 Key TakeAways, Exacta Disc Spreaders
The CentreFlow spreading system: prevents fragmentation of the granules due to impact with the vanes and maintains the spreading characteristics of the material.
EasySet: The compact ‘dashboard’ on each disc has considerably simplified accurate setting and adjustment of application rates.
The Exacta-CL EW, CL W PRO, CL GEOSPREAD® and Exacta-TL, TL/TLX GEOSPREAD® (iDC) are ISOBUS compatible & AEF certified as standard: simple plug and play possible.
Easy to assemble aluminum hopper extension rims
(Exacta-CL, CL EW, CL W PRO, CL GEOSPREAD ®, HL, TL, TL/TLX GEOSPREAD ® iDC)
1
2
3
4

## Slide 205: Contact Details
Please contact the Crop Care team for more information:
Product Management, PAS, Marketing
Bert van der Horst (PAS) Bert.vander.Horst@kvernelandgroup.com +31 641 456 365
Nicolas Huguet (PAS) Nicolas.Huguet@kvernelandgroup.com +33 671 805 458
Pavel Dvořák (PAS) Pavel.Dvorak@kvernelandgroup.com +420 602 158 154
Daniëlle Dekker (junior PAS) Danielle.Dekker@kvernelandgroup.com +31 657297548
Linda Segers Linda.Segers@kvernelandgroup.com +31 252 662 106
Louise de Boer Louise.deBoer@kvernelandgroup.com +31 252 662 166
Jeroen van Turenhout (PM) Jeroen.van.Turenhout@kvernelandgroup.com +31 252 662 259
Merel Arink (junior PM) Merel.Arink@kvernelandgroup.com +31 630258410
Customer Care
Jan van Warmerdam Jan.van.Warmerdam@kvernelandgroup.com +31 626 423 540
Kim Meijs Kim.Meijs@kvernelandgroup.com +31 252 662 122
Kees Wijfjes Kees.Wijfjes@kvernelandgroup.com +31 252 662 269
Jowell Creton Jowell.Creton@kvernelandgroup.com +31 252 662 176
Bianca Buis Bianca.Buis@kvernelandgroup.com +31 252 662 174
Mariska van Amsterdam Mariska.van.Amsterdam@kvernelandgroup.com +31 252 662 235